Configuration Manual

PSW-2G4F

PSW-2G4F-Ex

PSW-2G+

PSW-2G6F+ (PSW-2G6F+M)

PSW-2G8F+

PSW-2G4F-UPS

PSW-1G4F

PSW-1G4F-UPS

PSW-2G2F+UPS

SWU-16 (SWU-16M)

Multifunction Gigabit Managed Switches

for IP Video Surveillance Systems

Manual Version 10

Firmware version 0.2.2

© Fort-Telecom, Perm

2017

Contents

Designations	4

1 Introduction	5

2 Switch features	6

3 Light indication	7

4 Reset and restart buttons	8

5 Switch management	9

5.1 Management interfaces	9

5.2 What you need to know before connection	9

5.3 Management by means of the Web interface	10

5.3.1 First connection to the switch	10

5.3.2 Network settings	12

5.3.3 Configuring user accounts	13

5.3.4 Device description	14

5.3.5 Telnet setting	14

5.3.6 SNTP setting	15

5.3.7 Web interface language setting	16

5.3.8 Port settings	17

5.3.9 Port status	18

5.3.9.1 Firmware update of the SFP module	19

5.3.10 Configuring the Event List	20

5.3.11 Configurating Syslog	22

5.3.11.1 Syslog message list	25

5.3.12 Configuring SMTP	26

5.3.12.1 Example of configuration with a dedicated mail server on the local network	27

5.3.12.2. Example of setting with an external mail server	30

5.3.13 Configuring the dry contacts	32

5.3.14 Configuring VLAN  802.1q	33

5.3.14.1 Example of VLAN configuration	34

5.3.15 Configuring Port Based VLAN	36

5.3.16 Configuring VLAN Trunking	37

5.3.17 Configuring QoS (Quality of Service)	37

5.3.17.1 General settings	38

5.3.17.2 Speed limit	39

5.3.16.3 Configuring Class of Service	40

5.3.17.4 Configuring Type of Service	41

5.3.18 Configuring STP and RSTP	42

5.3.19 Configuring IGMP	44

5.3.20 Configuring SNMP	47

5.3.20.1 Configuring SNMP v1	47

5.3.20.2 Configuring SNMP v3	48

5.3.21 MAC address filtering	49

5.3.21.1 List of blocked MAC addresses	50

5.3.22 Set up Camera Comfort Start	51

5.3.23 Camera Hanging Control settings	52

5.3.24 Link Aggregation	53

5.3.25 Port Mirroring	54

5.3.26 Events broadcasting to Teleport integration units	55

5.3.27 Cable Tester	57

5.3.28 Remote Ping	58

5.3.29 Switch statistics	59

5.3.29.1 Port Statistics	59

5.3.29.2 PoE Status	60

5.3.29.3 ARP Table	61

5.3.29.4 MAC Table	61

5.3.29.5 DNS Table	61

5.3.29.6 System log	62

5.3.30 Firmware Update	62

5.3.31 Save and restore settings	63

5.3.31.1 Save settings to file	64

5.3.31.2. Restore settings from the file.	64

5.3.31.3 Editing configuration file	65

5.3.32 Reset to factory settings	72

5.3.33 Reboot	72

5.3.34 Optional expansion board	73

5.3.34.1 Digital inputs	73

5.3.34.2 Relay outputs	74

5.3.34.3 Logic	74

5.3.34.4 RS485 output	75

5.3.34.5 Connecting electricity meters	76

5.4 Management via Telnet	78

5.4.1 Example of setting	80

5.4.2 Description of Telnet commands	82

5.4.3 The config group	84

5.4.3.1 Network settings (config ipif)	84

5.4.3.2 Configuring ports (config ports)	84

5.4.3.3 Configuring multicast (IGMP Snooping)	85

5.4.3.4 Configuring STP/RSTP	86

5.4.3.5 Configuring SNMP	87

5.4.3.6 Configuring Syslog	88

5.4.3.7 Configuring VLAN	88

5.4.3.8 Configuring SNTP	89

5.4.3.9 Setting the comfort start function for the cameras	89

5.4.3.10 Setting protection from hanging	89

5.4.3.11 Configuring dry contacts (digital inputs)	90

5.4.3.12 Configuring TFTP	91

5.4.3.13 Configuring events	91

5.4.3.14 Configuring user accounts	92

5.4.3.15 Configuring QoS	93

5.4.3.17 Configuring MAC address filtering	94

5.4.3.18 Configuring inputs of the expansion board	95

5.4.3.19 Configuring outputs of the expansion board	95

5.4.3.20 Configuring RS485	96

5.4.3.21 Configuring channel aggregation	97

5.4.3.22 Configuring port mirroring	98

5.4.4 Show group	98

5.4.4.1 View switch information	99

5.4.4.2 Viewing switch settings	101

5.4.5 Firmware update using TFTP	107

5.4.6 Saving and loading configuration and log via TFTP	108

5.4.6.1 Saving configuration	109

5.4.6.2 Restoring configuration	109

5.4.6.3 Saving system log	109

5.4.7 Saving settings	109

5.4.8 Reboot	110

5.4.9 Exit the management mode	110

5.4.10 Diagnostic functions	110

5.4.10.1 Ping utility	110

5.4.10.2 Cable tester	111

5.5 Management via USB console	113

6 Technical support	115

# Designations

The following designations are used in this manual:

| Designation | Meaning |
| --- | --- |
|  | WARNING sign |
| Basic Settings → Network Settings | Italics are used to show the path to the Web page in case of configuration using the Web interface |
| DEFAULT | Bold type is used to highlight an important parameter, value, button name, etc. |
| #IPADDRESS=[192.168.0.1] | Courier New font is used to highlight parameters in the setting file |
| <VALUE> | Angle brackets are replaced with the variable value in the console command |
| config syslog state <STATE> | Console commands are in bold and italics |
| config syslog state enable | The output of control commands is in italics |

# 1 Introduction

This manual describes the setting and administration process of TFortis PSW and SWU managed switches. For many protocols, configuration is based on specific examples.

All switches are similar in terms of the configuration process. Therefore we will consider the managed switch PSW-2G4F as the basic device in this manual. Differences for other series switches will be specified additionally.

This manual describes Web-based and telnet-based configuration process.

# 2 Switch features

TFortis PSW switches are all-weather managed PoE (or PoE+) industrial Ethernet switches for IP video surveillance systems.

TFortis SWU switches are managed Ethernet switches for 19’’ 1U rack mounting.

Supported functions and protocols:

- Integrated Web interface

- Telnet

- SNMP v1, v3

- control of camera hanging

- preliminary heating of the camera housings

- cable tester

- redundancy protocols STP(IEEE 802.1d),  RSTP(IEEE 802.1w)

- Port Based VLAN

- Static VLAN (IEEE 802.1q)

- Flow Control (IEEE 802.3x)

- Quality of Service (802.1p) (CoS, ToS(DSCP) )

- IGMP Snooping v2 multicast management

- SNTP

- SMTP

- Syslog

- system log

- DNS

- remote Ping function

- event notification settings

- firmware update using TFTP

- MAC filtering

# 3 Light indication

TFortis PSW switches have 2 LED indicators to show the operating mode of the switch processor: DEFAULT and CPU. (Figure 1.1, Table 1.1) (Descriptions and functions of other light indicators are available in Operating Manual, Section 2.7, Configuration and control elements).

Figure 1.1 DEFAULT and CPU indicators – PSW switch

Figure 1.2 DEFAULT and CPU indicators – SWU switch

Table 1.1 Purpose of indicators

| Indicator status | Device status |
| --- | --- |
| CPU indicator flashing slowly (at 1 Hz) | Normal operation |
| DEFAULT indicator on | The device is not configured, with factory-default settings. |
| CPU indicator flashing rapidly (at 10 Hz) | Indication of camera hanging (or there is no link on the video camera port or the camera does not respond to Ping), or indication of dry contacts active status. |
| CPU and Default indicators flashing in sync | Hardware or software fault is detected. Contact technical support. |

# 4 Reset and restart buttons

TFortis PSW switches have 2 hard buttons to restore factory default settings and to restart the device. Location of the buttons is shown in Figure 1.1.

- To restart the switch, press CPU button shortly.

- To restore factory settings, press DEFAULT button and hold it down for about 30 seconds. DEFAULT indicator should set ON at this point.

TFortis SWU switches have one hard RESET button.

- To restart the switch, press the RESET button and hold it down for 3-5 seconds.

- To restore default settings, press the RESET button and hold it down for 30 seconds.

# 5 Switch management

## 5.1 Management interfaces

PSW and SWU switches have the following options of remote management: Web interface, Telnet, SNMP. It is also possible to manage the switch using a local USB console.

Web interface contains a full set of managed parameters with a detailed explanation and a short summary. The switch interface is available in Russian and in English. Connection to the switch is possible using a standard Web browser.

Telnet is an alternative way of device configuring using a console application, such as Microsoft Telnet, PuTTY, Hyper Terminal or others.

Management by means of SNMP is currently implemented in the test version and not all commands are supported in full. SNMP is recommended for monitoring rather that management of the switch.

Management by means of the USB console has the same console interface as Telnet interface.

## 5.2 What you need to know before connection

Attention!

TFortis PSW switches have an integrated PoE injector on Fast Ethernet ports.  It means that 48~55 V voltage can be supplied to these ports.

Before connecting the IP cameras, make sure that PSW port parameters correspond to the camera parameters.

Before connecting network devices that do not support PoE (such as a computer or laptop) to the Fast Ethernet port, disconnect the PoE on this port by removing the jumpers. For more information about PoE hardware configuration, see Operating Manual, Section 2.3.

Attention!

Power supply elements are under high voltage.  It is strictly forbidden to touch conducting elements of the power supply unit under voltage.

## 5.3 Management by means of the Web interface

### 5.3.1 First connection to the switch

When switched on for the first time, the switch has the following default settings:

IP address: 			192.168.0.1

Subnet mask:		255.255.255.0

Login/password		not set

Management VLAN 	1

DHCP client		off

STP				off

Telnet			on

SNMP			off

Before connecting, make sure that the network card of the computer is on the same subnet as the switch (192.168.0. *).

Start the Web browser and enter the IP address of the switch in the address bar (Figure 5.3.1.1).

Figure 5.3.1.1 Connection to the switch

After connection, main Web interface page should display (Figure 5.3.1.2).

Figure 5.3.1.2 Web interface

The Web interface can be divided into 4 frames shown in Figure 5.3.1.2:

1 – side menu that provides access to various groups of settings

2 – main frame containing the group of settings

3 – help for these settings

4 – header with link status and PoE on the ports (automatically updated every 10 seconds)

Note: by default, access to Web interface is available without login and password. It is recommended to restrict access in the future by setting login and password.   In this case each subsequent connection to the switch will be accompanied by a standard authentication dialog box.

### 5.3.2 Network settings

Basic Settings → Network Settings

This section describes the basic network settings of the switch.

Figure 5.3.2.1 Network settings

MAC – the physical address of the device used to identify the device in the network. It is not recommended to change the MAC address otherwise than in extreme cases, since it ensures uniqueness of the switch. The last 2 bytes of the factory MAC address are the serial number of the device. The factory MAC address is printed on the label and placed on the enclosure and on the circuit board of the switch.

IP – the network address of the device. When working within the same subnet, it is necessary to ensure the uniqueness of the network address.

Mask – the subnet mask.

Gateway – gateway network address. If the gateway is not used, leave the default value: 255.255.255.255

DNS – network address of the DNS resolver. It is used in some functions to convert the host name to its network address. If not used, leave the default value: 255.255.255.255

DHCP Mode – selecting the operating mode of the DHCP protocol:

1. Disable – DHCP disabled. The switch uses static network settings (IP, Mask, Gateway and others).

2. Client – DHCP mode enabled. The switch receives network settings automatically using broadcast request to the DHCP server.

### 5.3.3 Configuring user accounts

Basic Settings → User Accounts

This section contains the settings of user accounts.

Figure 5.3.3.1 List of users

By default, the only account is the administrator account with an unset user name and password. It means access to Web interface and Telnet is available without authentication.

To restrict access, it is necessary to create at least one user with Admin rights and one or more users with User rights, if necessary.

Access rights are separated by selecting the Access Right field.

Figure 5.3.3.2 Configuring user name and password

The user with Admin rights has maximum authorities.

A user with User rights has limited authorities, cannot change settings and has access to switch statistics and diagnostic tools (Ping, Virtual Cable Tester).

If setting was successful, the message "Parameters accepted" will be displayed and it will be necessary to log in using the login and password.

If an error message is displayed, enter the parameters again.

Note 1: These fields are mandatory. The maximum length is 20 characters. Input language is English.
Note 2: The fields are case sensitive, i.e. there is a difference between "Admin" and "admin".

Note 3: Up to 4 accounts are supported.

### 5.3.4 Device description

Basic Settings → Device Description

Figure 5.3.4.1 Device description

Device Name – device name

Device Location – device location

Service Company – contact information of the service company or responsible person

These fields are optional and only serve to simplify the identification of the switch. The maximum length of entries is 64 characters in English and 32 characters in Russian.

### 5.3.5 Telnet setting

Basic Settings → Telnet

Figure 5.3.5.1 Enabling Telnet and TFTP

Telnet – protocol used for remote management of network equipment based on port 23 TCP protocol.

By default, Telnet is enabled. If necessary, it may be disabled.

The login and password for Telnet access are the same as for the Web interface access.

Option Echo is an option of Telnet protocol enabled by default.

In addition, the switch firmware may be upgraded using Telnet, in this case the switch uses TFTP protocol.

Since TFTP protocol is not secure, it is disabled by default. If necessary, it is possible to enable it, or change the standard UDP port (69) for another one.

For more details on configuring with Telnet, see Section 5.4.

### 5.3.6 SNTP setting

Basic Settings → SNTP

Figure 5.3.6.1 SNTP setting

SNTP (Simple Network Time Protocol) is the protocol by which the switch synchronizes its internal clock with an external time server.

The switch does not contain a built-in real-time clock, so it is necessary to use SNTP protocol to get information about the current time. The use of SNTP protocol is not mandatory and the main functions of the switch are not connected with SNTP. However, to simplify administration, the switch supports the recording of the event log in the "black box" and sending syslog and e-mail messages about the events to the network administrator. With SNTP protocol enabled, these messages will include a time stamp, which can be helpful for the administrator servicing the network.

Settings:

State — state

Server IP address – IP address of SNTP server

Server Name – domain name of SNTP server. If both IP address and domain name of the server are set, IP address will prevail

Time Zone – time zone (difference from UTC)

Period – time period of synchronization with the server (in minutes)

Synchronize – forced synchronization of time (to check the settings)

### 5.3.7 Web interface language setting

Basic Settings → Language

Figure 5.3.7.1 Language selection

The Web interface of the switch supports 2 languages: Russian and English. The default language is English. You may change it to Russian, if necessary. To do that, make sure there are no problems with text encodings in the browser.

Web interface of the switch uses UTF-8 encoding.

### 5.3.8 Port settings

Ports → Port Settings

Figure 5.3.8.1 Port settings

The following port parameters can be set:

1. State – Port status. The port can be forced to switch off, if it is not used. In this case, the port will not transfer data and the port link will not come up.

- Speed/Duplex – Speed/Duplex. By default, the auto negotiation mode is set which automatically adjusts the speed and duplex mode. Speed and duplex can be set manually, however in this case it is important to make sure that the remote side will accept such settings. For Gigabit Ethernet ports, control of port status and speed is not available.

- Flow Control – control of data flow (IEEE 802.3x)

- PoE – Power over Ethernet. For some switch models, it is possible to manage PoE only using option A (protocol PoE). To manage PoE using option B (Passive PoE), it is necessary to move the corresponding jumpers on the board.

To configure PoE using jumpers, see Operating Manual, Section 2.7, Configuration and control elements.

5. SFP Link Mode – the operating mode of SFP (optical) port link.

  - Forced – forcing the link to come up when an optical signal is detected (Default mode)

  - Auto – automatic mode, recommended when connecting to third-party equipment

### 5.3.9 Port status

Ports → Port Status

Figure 5.3.9.1 Port status

The following port parameters are available:

- State – port state: on/off/blocked (with RSTP protocol off)

- Link – Link status

- Speed/Duplex – Speed/Duplex

- Flow Control – control of data flow (IEEE 802.3x)

- PoE – Power over Ethernet.

- SFP – Additional information about connected SFP modules Information from the internal memory of the SFP module is displayed, which is security-programmed by the manufacturer. The "Detail" button becomes active when the module is connected.

Warning: this information is indicated by the SFP module manufacturer. However, since this information is optional, the manufacturer may not provide it or provide inaccurate or incorrect information. Therefore, this information should be seen as additional, rather than primary.

Figure 5.3.9.2 Information from SFP module

#### 5.3.9.1 Firmware update of the SFP module

The switches provide for SFP modules flashing. It may be necessary when using third-party modules in the switches of some vendors (such as CISCO, HP).

Figure 5.3.9.3 SFP module flashing interface

Firmware Dump – saves the current firmware of the SFP module to a file. When flashing, it is strongly recommended to dump the old firmware in order to have the ability to rollback, i.e. return to the old version.

Preloaded Firmware Download – a list of preloaded firmware for modules with the wavelengths of 1550 and 1310 nm. This list contains the latest firmware at the time of the switch firmware release.

Custom Firmware Download – download a third party firmware file.

Warning: the possibility of reprogramming depends also on the SFP module type. There are modules whose memory only works in read-only mode. Such modules cannot be reprogrammed.

### 5.3.10 Configuring the Event List

Events → Event List

The PSW switch has a wide range of capabilities to ensure convenient network administration and network functionality. A key feature of the switch is the ability to provide instant administrator notifications about the events through various tools, such as Syslog, SMTP (e-mail) or SNMP Trap.

The switch may be adjusted to respond only to certain events to which an appropriate level of significance is assigned (only for the Syslog protocol). Levels range from 0 to 7, where 0 is the highest level of significance.

The following range of levels is generally accepted:

- (0) Emergency: the system is inoperable

- (1) Alert: the system requires immediate intervention

- (2) Critical: the state of the system is critical

- (3) Error: error messages

- (4) Warning: warnings about possible problems

- (5) Notice: messages of normal, but important events

- (6) Informational: information messages

- (7) Debug: debugging messages

Such separation of events significance levels allows to process the events differently on the server side. For example, messages about level 6 and 7 events can simply be recorded in the event log, while messages about level 0-3 events will be shown to the operator.

The settings are divided into subgroups by the following categories:

- Port.link – change the status of the link

- Port.PoE – change the status of PoE

- STP/RSTP – change STP/RSTP topology

- Autorestart.Link – the link is lost with the Auto Restart function active

- Autorestart.Ping – the remote device did not respond to PING with the Auto Restart function active

- Autorestart.Speed – activity on the port fell below the preset value with the Auto Restart function active

- System – change the system state (restart, update, reset to factory settings, etc.)

- UPS – changes in the operation of the UPS (only in the version with the UPS)

- Inputs/Outputs – event from the access control system (dry contacts and tamper sensor)

- MAC Filtering – an attempt was made to access the switch from a MAC address that is not included in the list of allowed (if MAC address filtering is enabled)

The following events are active by default:

- changing the link,

- a link was lost with the Auto Restart function active, or the device did not respond to the PING, or the speed on the port fell below the preset level

- change in the operation of the UPS module (switching to battery power, etc.) (only in the version with UPS module available)

- events from the access control system.

When using the default configuration, you receive only the most significant information regarding the proper functioning of the system. Less significant messages are not shown.

Figure 5.3.10 Events list

### 5.3.11 Configuring Syslog

Events → Syslog

Syslog – the standard for sending messages about the events occurring in the system (logs) used in IP networks. Syslog protocol is simple: when certain events occur, the PSW switch sends a short text message, less than 1024 bytes in size, to the recipient of the message. Messages are sent by UDP (port 514).  Syslog is used for ease of administration and information security.

The switch may be adjusted to respond only to certain events to which an appropriate level of significance is assigned. (Tab Events → Event List)  Levels range from 0 to 7, where 0 is the highest level of significance.

The following range of levels is generally accepted:

- (0) Emergency: the system is inoperable

- (1) Alert: the system requires immediate intervention

- (2) Critical: the state of the system is critical

- (3) Error: error messages

- (4) Warning: warnings about possible problems

- (5) Notice: messages of normal, but important events

- (6) Informational: information messages

- (7) Debug: debugging messages

Such separation of events significance levels allows to process the events differently on the recipient side. For example, messages about level 6 and 7 events can simply be recorded in the event log, while messages about level 0-3 events will be shown to the operator.

Syslog message format

According to the Syslog standard, the message has the following format:

<significance level> <date and time> <sender's IP address> <message>

Note: the <date and time> field shows the date and time received by the SNTP protocol. If no time data is received or SNTP is not configured, the <date and time> field will show the time in seconds after the switch is turned on.

Here is an example to illustrate that: We have a message, received over Wireshark:

Figure 5.3.11.1 SNTP is not configured

As we see, the time has not been set. The time after switch start is shown.

_Figure 5.3.11.2. SNTP is configured

Now the message has a standard time stamp.

Configuring Syslog on the switch

Configuring on the switch is rather simple. First, select the necessary events in the Events → Event List tab. For example, we are interested in the link change event.

Figure 5.3.11.3 Select the event

Then go to the Events → Syslog Settings tab and enable the Syslog protocol and set the IP address of the server to which messages will be sent.

Figure 5.3.11.4 Configuring Syslog

Getting Syslog messages

After configuring the switch, proceed to configure the server.

Let's consider an example for Windows OS. There are a lot of programs for working with syslog-messages, such as:

- Kiwi Syslog

- Syslog Watcher

- Datagram SyslogServer Suite

- syslogbroadband

- LogZilla

- Syslog Server Free Tool

Let's choose Kiwi Log Viewer. This is a free simplified version of Kiwi Syslog Server. Nevertheless, it is fit for purpose in our case.

Download address is http://www.kiwisyslog.com/downloads.aspx

The installation of the program is rather simple. The main thing is to choose "Install as Service" in the "Choose Operating Mode" window (in this case, Kiwi Syslog will be installed as a service: it will start as the OS starts and will reside in the tray).

Figure 5.3.11.5 Kiwi Syslog installation

After installation, start the program. By default, all received messages will be displayed in the main window. These messages are recorded to a text file. It is also possible to configure forwarding by email.

Figure 5.3.11.6. Kiwi Syslog interface

#### 5.3.11.1 Syslog message list

Table 5.3.1 Syslog message list

| Port #1 Link Up/Down | Link changed |
| --- | --- |
| Port #1 PoE A Up/Down | PoE changed |
| STP topology changed: root port 1, root bridge MAC 01:02:03:04:05:06 | STP/RSTP topology changed with root port and MAC indication |
| Port #1 Autorestart: no link | No link with the enabled control of camera hanging by link criterion |
| Port #1 Autorestart: no reply to Ping | No response to PING requests with enabled control of camera hanging by PING criterion |
| Port #1 Autorestart: Low Speed | Low speed through the port with enabled control of camera hanging by SPEED criterion |
| Web-interface authentication: Ok | Login to the WEB-interface with a password |
| Update firmware x.x.x | Firmware update |
| Default settings | Reset to factory settings |
| Clear ARP cash | Clear the ARP cache of the switch |
| Start after power reset | PSW start after power reset |
| Start after reset | PSW start after reset |
| Voltage on battery is low (below 44V) | Low battery voltage, below 44V |
| Power souce is battery/ Power souce is external VAC | PSW power source (battery or external VAC) |
| Sensor 0 (Tamper) is active! | Tamper sensor is active (for PSW-2G + and PSW-2G6F +) |
| Sensor 1 (Dry contact) is active! | Sensor input (dry contact) is active |
| Input 1 is active (Open) | Output 1 is active (with current state indication) |
| Unallowed MAC: 01:02:03:04:05:06 Port 1 | Unallowed MAC at port 1 |
| Port 1 Error-Disabled | Port 1 is in the Error-Disabled state |

### 5.3.12 Configuring SMTP

Events → SMTP

Short list of terms

SMTP – (Simple Mail Transfer Protocol) protocol for sending e-mail messages over the network. SMTP is used to send messages to a mail server. To receive messages from the mail server, client applications typically use POP or IMAP protocols.

Settings:

State — SMTP state

Server IP address – IP address of the mail server

Server domain name – domain name of the mail server

Port – number of TCP port through which messages are sent (0 – 65534). By default 25.

Sender e-mail address – e-mail address of the sender. Shown in the From field in the e-mail

Receiver e-mail address – e-mail address of the receiver. Shown in the To field in the e-mail. For additional user opportunities, up to 3 receivers are available.

Subject – subject of the e-mail.

Login, Password – login and password if the server requires authentication.

If these fields are filled in, the authentication with the server will be automatically activated. If these fields are empty, authentication will not be required.
PSW switch supports AUTH PLAIN and AUTH LOGIN authentication.

If server IP address is not specified, messages are sent to this address by default. To use the domain name, set Server IP address in 0.0.0.0 and specify the domain name in the Server domain name field.

Examples of SMTP configuration

There are two options for configuring e-mail:

- A dedicated mail server is located on the local network.

- An external mail server is used.

Each option has its advantages and disadvantages. A dedicated mail server can be recommended if video surveillance network is physically separated from the Internet and it is impossible to use external mail services, or there is already a mail server on the network and no additional efforts are required to create and maintain the server. Using external mail services makes configuration easier and faster, eliminates the need to maintain a mail server, but in this case you need a permanent connection to the Internet, which may not always be possible because of enterprise security policies.

#### 5.3.12.1 Example of configuration with a dedicated mail server on the local network

Figure 5.3.12.1.1 Network structure

Let's formulate the task as follows:

We need to configure SMTP on switch SW2 (PSW-2G) with IP 192.168.0.1 to send messages about the link change on the ports of PSW-2G switch to operator's computer 192.168.0.3.

Since the SMTP protocol does not involve storing messages and issuing them to the mail client, we need to include a mail server (192.168.0.2) into the network.

We select the domain name companyname.com for the network

We select the e-mail address psw2g@companyname.com for PSW-2g,

server@companyname.com for SMTP server,

and client@companyname.com for the client.

Configuring PSW

First, specify the event that will send a message when it occurs. In our case, this event is a link change. To do this, tick the appropriate event in the Events → Event List tab.

Figure 5.3.12.1.2 Select the event

Now let's configure the SMTP

Go to Events → SMTP tab.

Enable SMTP, set the IP address of the server,

set the e-mail address of the sender (i.e. PSW) psw@companyname.com,

set the e-mail address of the main receiver server@companyname.com,

set the backup address server2@companyname.com to which the messages swill be duplicated.

E-mail subject is "PSW-2G log".

Leave the Login and Password fields empty, since we are not going to use authentication.

Figure 5.3.12.1.3 Configuring SMTP in PSW

Press "Apply". Now the settings are applied.

Now let's configure the mail server

There are a number of mail server programs for various operating systems that support various protocols. We need a program that supports SMTP and POP3.

As an example of mail server for Windows, let's see Office Mail Server (https://www.box.com/oms). This is a free program with simple configuration.

Technical support and instructions are available on the website: http://oficemailserver.livejournal.com/

Install the program. After startup, the main window will be available:

Figure 5.3.12.1.4 Office Mail Server main window

Go to menu Options->SMTP/POP3 server options and select

Local domain name: companyname.com

In the Users field add the user client. Then select user type [BOSS].

Office Mail Server supports the following types of users:

- Postmaster — a user responsible for Office Mail Server operation and maintenance. This user receives special messages generated by the system in case of an error.

- Daemon – this is used to remotely connect to an external SMTP/POP3 server, send and receive messages

- Boss – this is the user who gets copies of all messages sent over the SMTP server.

Figure 5.3.12.1.5 Office Mail Server configuration

In Options->Transaction options tab:

Set the IP address of the server, check the box "Automatically send outbound message if found", disable SMTP authorization (SMTP login button)

Figure 5.3.12.1.6 Configuring Office Mail Server

Now all the messages coming to the server will be forwarded to client@companyname.com

Configuring client

Configuring client is rather simple. Example of configuring using Mozilla Thunderbird:

Figure 5.3.12.1.5 Configuring the mail program Mozilla Thunderbird

After finishing all the settings, you can go to the Web-interface to the SMTP Settings tab and check by sending a test message. Fill in the field Subject and Message and send out the message. If the settings are correct, Mozilla Thunderbird will notify of the new message.

Figure 5.3.12.1.6 Sending a test message

#### 5.3.12.2. Example of setting with an external mail server

Figure 5.3.12.2.1 Sample network topology

In this example we will see how to configure PSW when an external mail server is used.

Let it be a mail server mail.ru. The procedure will be similar for other servers that support AUTH PLAIN or AUTH LOGIN authentication.

We will need to create a mail account and select the SMTP connection settings. For mail.ru – the address of SMTP server is smtp.mail.ru, port 25.

Now we can start configuring.

Fill in the information according to Figure 5.3.12.2.2.

Address for sending messages is companyname@mail.ru,

Let the recipient address be the same, as if we are sending an e-mail to ourselves.

Login: companyname@mail.ru (at mail.ru login is the address itself)

Password: password

Note: in this example we fill in the Server domain name field and fill the Server IP address with zeros. In this case, the switch will receive the IP address of the server automatically through the DNS query, but for this purpose the DNS address of the resolver must be configured. If DNS is not configured, it will be necessary to directly specify the IP address of the SMTP server.

Figure 5.3.12.2.2 Configuring SMTP in PSW

After finishing all the settings, you can go to the Web-interface to the SMTP Settings tab and check by sending a test message. Fill in the field Subject and Message and send out the message.

Figure 5.3.12.2.3 Sending a test message

### 5.3.13 Configuring dry contacts

Special Functions → Inputs/Outputs

Depending on the model, PSW switches are equipped with connectors for contact sensors (dry contacts) and/or built-in tamper sensor. They can be used for security purposes, for example for access control.

There are two ways of sending out an alarm event:

- Over Syslog, SMTP, SNMP Trap protocols. When a dry contact is triggered, a message is generated, which is sent to the server which receives and logs the message and informs the operator.

- Using the Teleport-1 integration units, which have digital outputs, it is possible to configure the transfer of the dry contact activation in PSW switch to the output in the Teleport integration unit. In other words, if the switch input is closed and the switch is remote from the server, the output of the Teleport integration unit installed in the server room will be closed simultaneously. The output can then be connected to any security system. The configuration of the PSW-Teleport link is discussed in detail in section 5.3.26.

Figure 5.3.13.1 Configuring dry contacts

- State – enables input operation. An alarm message will be sent, if State is in the Enable state, and Current State matches Alarm State and a tick is set in Inputs/Outputs in the Events List tab.

- Alarm State – state of the input that is considered to be an alarm.

- Open – open state

- Short – closed state

- Current State – current input state.

### 5.3.14 Configuring VLAN  802.1q

VLAN → 802.1q Static VLAN

Terms and abbreviations:

VLAN (Virtual Local Area Network) — a group of devices that have the ability to interact directly with each other at the link layer, although physically they can be connected to different network switches. Conversely, devices in different VLANs are invisible to each other at the link level, even if they are connected to the same switch, and communication between these devices is possible only at the network and higher levels.

VID (VLAN ID) – virtual network ID

VTU (VLAN Table Unit) – a table containing the list of virtual networks configured on this switch

Management VLAN ID – VLAN ID for the management network. Access to Web-interface is only possible from this network.

VLAN List – a table containing information about the virtual networks configured on the switch, states and ports belonging to this VLAN.

VTU Table – VTU (VLAN Table Unit) – table for editing virtual networks, information in this table contains the following fields:

- VID (VLAN ID) – virtual network ID.

- State — state. The created VLAN can be temporarily disabled by selecting the Disable state.

- VLAN Name – virtual network ID (up to 16 characters). This field is used only for convenience of configuration and is not mandatory.

Port state in this VLAN. A port may be in one of the 3 states:

- NoMem (Not a member) – a port is not a member of this VLAN.

- UnTag (Untagged) – untagged port (access port) allows to combine selected ports into one VLAN.

- Tag (Tagged) – tagged port (trunk port). Several VIDs can be set for a tagged port.

To finally apply settings, press Apply button.

The switch support up to 100 different VLANs.

#### 5.3.14.1 Example of VLAN configuration

Let's configure the virtual networks as shown in the scheme.

Figure 5.3.14.1 Network topology

Where VLAN 1 is the management network that will be used to connect switches SW1, SW2, SW3 to the Web-interface.

VLAN 2 and VLAN 10 are user's VLANs

Let's start configuring from the most remote switch SW2.

Ports FE1, FE2 belong only to VLAN2 and are connected to terminal devices, therefore these ports are untagged. The same is true for port FE3 which belongs only to VLAN10. Port GE1 belongs to 3 VLANs: VLAN1, VLAN2, VLAN10, therefore it is a tagged port.

Based on the above, we will select the following settings:

Figure 5.3.14.2 SW2 settings

Press the Apply button. Connection with the device will be lost.

Now let's configure SW3 switch.

We select the following settings:

Figure 5.3.14.3 SW3 settings

Press the Apply button. Connection with the device will be lost.

Now let's configure SW1 switch.

We select the following settings:

Figure 5.3.14.2 SW1 settings

Press the Apply button. Connection with the device will be lost.

After setting up the last switch, we must go to the Web interface of switches SW1, SW2, SW3 from a PC connected to the FE1 port of the switch SW1. It will not be possible from other ports.

### 5.3.15 Configuring Port Based VLAN

VLAN → Port Based

Port Based VLAN is the simplest way for organizing virtual networks by differentiating access at the level of the switching matrix of the switch. Port Based VLAN does not use packet tagging. Each individual port may belong only to one VLAN.

Attention!

Port Based VLAN is available only for outdoor PSW switches

Port Based VLAN is configured as follows:

- Enable Port Based VLAN.

- Check the corresponding boxes of the switching matrix.

- Apply settings (Apply)

Example.

It is necessary to configure 2 virtual networks: VLAN1 – ports 1 and 2, VLAN2 – ports 3 and 4. Check the boxes as shown in the Figure below.

Figure 5.3.15.1 Example of Port Based VLAN configuration

### 5.3.16 Configuring VLAN Trunking

VLAN → VLAN Trunking

Enabling the VLAN Trunking function on the port means that any VLANs are allowed to go through this port, except for those that are statically set up (the VLAN → 802.1q Static VLAN tab). In other words, only unknown VLANs go to the port with the VLAN Trunking function enabled, others VLANs operate according to the settings, because they are included into VLAN and ports tables.
	The purpose of this function is as follows: if the switch is between two devices that form VLANs (for example, dynamic VLANs that need to be transparently connected to other parts of the network), then it is enough to enable VLAN Trunking on two ports and the switch will let them go through. Otherwise it would be necessary to input all possible VLANs into the table.

Figure 5.3.16.1 Configuring VLAN Trunking

To enable the VLAN Trunking function, set the state switch into enable position and check the boxes of the required ports.

If only static VLANs (802.1q) are used, activation of the VLAN Trunking function is not required!

### 5.3.17 Configuring QoS (Quality of Service)

Using IEEE 802.1p QoS allows to prioritize traffic and allocate the necessary bandwidth for applications sensitive to delays, including VoIP (Voice over IP) and video conferencing. The required bandwidth is created by reducing the transfer rate of applications that are not sensitive to delay.

The switch organizes 4 separate hardware queues on each physical port. Packets received from different applications receive the corresponding priority.

The switch supports 3 types of priority:

1) by the number of port

2) by CoS label

3) by ToS (DSCP) label

#### 5.3.17.1 General settings

QoS → General Settings

Select basic settings on the "General settings" tab

Figure 5.3.17.1.1 Configuring QoS

State – enable/disable QoS operation

QoS Scheduling mechanism – queue scheduling type:

  - Weighted fair priority – packets with different priority are processed by the switch with the ratio 8: 4: 2: 1. It means, the switch will process 8 high priority packets, 4 medium priority packets, 2 low priority packets and 1 packet with the lowest priority in one time unit.

  - Strict priority – packets with a higher priority will be processed first, until the high-priority packet queue becomes empty. Meanwhile, packets with lower priority will be in the queue.

Weighted fair priority is recommended by default.

Priority mode – priority for choosing CoS or ToS.

- CoS only – only CoS is active and the package priority is determined only by the CoS (Class of Service) field in the Ethernet frame.

- ToS only – only ToS is active and packet priority is determined only by the ToS (Type of Service) field in the IP header.

- CoS & ToS – both CoS and ToS services are active, but if a packet containing both priority fields comes in, the priority is selected by the ToS field.

Default priority – priority by default. When the QoS mechanism is active and a packet that does not contain a priority field comes in, it is given the corresponding default priority by CoS and it is treated as a tagged packet with the appropriate priority. 

	There are 8 CoS priorities. Priorities are numbered from 0 – lowest priority to 7 – highest priority.

#### 5.3.17.2 Speed limit

QoS → Rate Limit

Figure 5.3.17.2.1 Configuring speed limit

A configurable limit on the maximum receive and transmit rate for each port is available.

RX limit – limit of incoming traffic in Kbps 
TX limit – limit of outgoing traffic in Kbps 

Note 1: The speed limit is available in the range from 64 Kbps to 102400 Kbps for FastEthernet ports and up to 256000 Kbps for Gigabit Ethernet ports.
Note 2:  If the port operates without limit, set the RX limit and TX limit fields to 0

#### 5.3.17.3 Configuring Class of Service

QoS → CoS

Figure 5.3.17.3.1 Configuring CoS

The Class of Service (CoS) field is 3 bits in the 802.1Q tag of the Ethernet frame. It allows to divide traffic into 8 priorities with different markings at the link level. The switch supports 4 queues of service: Queue 0 – Queue 3. Queue 3 is the queue with the highest priority, Queue 0 is the queue with the lowest priority. 
	The setting will apply, if you set the value of CoS State to Enable in the QoS General Settings tab.

By default, the priorities are sorted by queue as follows:
			Priority 0 belongs to Queue 1
			Priority 1 belongs to Queue 0
			Priority 2 belongs to Queue 0
			Priority 3 belongs to Queue 1
			Priority 4 belongs to Queue 2
			Priority 5 belongs to Queue 2
			Priority 6 belongs to Queue 3
			Priority 7 belongs to Queue 3

#### 5.3.17.4 Configuring Type of Service

QoS → ToS

Figure 5.3.17.4.1 Configuring ToS

Type of Service (ToS) – field in the IP-header (1 byte). It is intended for marking traffic at the network level. PSW switches can operate with IP packets, which have the appropriate field in the header – IP Type of Service (ToS), one byte in size. ToS is filled with the DSCP classifier.

The setting will apply, if you set the value of CoS State to Enable in the QoS General Settings tab.

By default, the priorities are sorted by queue as follows:
	Priorities 0-7 belong to Queue 0
	Priorities 8-31 belong to Queue 1
	Priority 32-55 belong to Queue 2

Priorities 56-63 belong to Queue 3

### 5.3.18 Configuring STP and RSTP

STP/RSTP → RSTP Settings

Figure 5.3.18.1 Ring topology

To ensure the protection of communication channels from a single failure, they must be backed up. Reservation inevitably leads to the emergence of ring sections of the network – closed routes. The Ethernet standard provides for a tree topology only and does not allow ring-type topologies, as this leads to looping of packets.

PSW switches support Spanning Tree Protocol (STP, IEEE 802.1d), which allows to create ring routes in Ethernet networks. STP continuously analyzes the network configuration and automatically builds a tree topology, transferring redundant communication lines to the reserve. In case of a violation of the integrity of the network constructed in this way (for example, a break in the optics), STP includes the necessary backup lines in a few seconds and restores the tree structure of the network.

In addition, PSW switches include a more powerful version of this protocol – Rapid Spanning Tree Protocol (RSTP, IEEE 802.1w), which allows to reduce network rebuild time to several milliseconds. When using RSTP, a break in the optics results in a short-term fading of the picture from the video camera (less than 1 second), followed by the restoration of normal operation.

It's important to remember, that IEEE802.w Standard does not recommend to include more than 7 switches into a single ring with standard parameters of RSTP protocol.

Configuring RSTP

To simplify the configuration process, most parameters are hidden. In general, you do not need to change all the variables. All you need to do is to enable RSTP and specify Bridge Priority, if required.

Figure 5.3.18.2 RSTP basic setting

To get access to all available RSTP configuration variables, click on the "Advanced Settings Show" button.

Figure 5.3.18.1 Advanced RSTP settings

Variable available for editing:

- RSTP State – off mode, STP or RSTP.

- BPDU Forward

- Bridge Priority – the priority of the bridge (switch), is set in steps of 4096 (1-32768). It is required to determine Root Bridge (of the root switch). The root switch is the one with the lowest Bridge Priority value.

- TX Hold Count –  limit the maximum number of BPDU packets sent per second (1-10).

- Bridge Max Age – time of waiting for the bridge in seconds, after which it sends a message about rebuilding of the network (6-40 seconds).

- Bridge Hello Time – the period of sending BPDU packets in seconds (1-2 seconds).

- Forward Delay Time – the delay of transition of port states from the Listening and Learning state to the Forwarding state (in seconds) (4-30). 

Port settings:

- RSTP State – including the port in the STP / RSTP protocol. If support of the ring topology on a specific port is not required, this port can be excluded from RSTP. However, note that if this port becomes a backup line, this may lead to the looping of packets and a storm.

- Port Priority – port priority (0-240) changes in steps of 16.

- Cost – the cost of the port's path (1-200000000). If there are several alternative paths, the one with the minimum sum of the cost of path is always chosen. The cost of the port depends on its throughput, for the FastEthernet port it is 200000, for the port GigabitEthernet it is 20000.

- Auto cost – select the cost of the port path. The cost of the path is chosen based on the port's throughput. If the tick is not set, the cost of the path is taken from the Cost field.

- Edge – manual or automatic detection of the edge port.  Edge port is a port that directly connects to a network segment,

where the creation of a loop is impossible.  An example of an edge port is a port directly connected to a workstation. Ports configured as edge ports go into the packet propagation state immediately, bypassing the listening and learning states.  The edge port loses its status immediately as soon as it accepts a BPDU package, becoming a usual spanning tree port.

- PTP – manual or automatic detection of a point-to-point connection, that provides a quick transition to the mode of packet propagation. The P2P port is used to connect to other bridges.

When setting Forward Delay Time, Bridge Hello Time, Bridge Max Age, the following condition should be met:

2*(Forward Delay Time - 1) >= Bridge Max Age >= 2*(Bridge Hello Time + 1).

After configuring RSTP, check the resulting topology in the RSTP Status tab.

### 5.3.19 Configuring IGMP

IGMP → IGMP Snooping

Figure 5.3.19.1 Basic settings of IGMP Snooping

IGMP snooping is designed to prevent broadcasting of multicast traffic from being relayed to consumer computers that do not explicitly claim to be interested in it. This allows the switches to exclude such traffic from the streams sent through ports to which its consumers are not connected, thereby substantially reducing the network load.

Basically, to enable IGMP snooping, you only need to turn it on. That is why the majority of the settings are hidden. To see all the settings, click the button "Advanced Settings Show"

Figure 5.3.19.2 Advanced IGMP Snooping settings

- IGMP Snooping state – state of IGMP protocol

- Send IGMP Query – Send General Query. (It is possible to disable the sending of General Query)

- Query Interval – the interval between sending Query messages (1-255 seconds). 60 seconds by default.

- Query Response Interval – the maximum time to wait for a response from the host to send periodic public queries (1-25 seconds). 10 seconds by default.

- Group Membership Interval – the interval while the router is waiting for an IGMP Report. If the report was not received, then the router believes that there are no more hosts on the network that belong to the group (1-255 seconds). 250 seconds by default.

- Other Querier Present Interval – if the switch is Non-Querier, then if it has not received a Query during this interval, it starts to consider itself a Querier. 255 seconds by default.

- Port State – IGMP Snooping activity on the selected port. If the box is checked, IGMP is active on the port. If the box is not checked, the port returns to the normal operating mode (i.e. the port will perceive all multicast traffic as broadcast)

Note: IGMP Snooping only works with traffic from the management VLAN.

To see a list of the current multicast groups, go to the IGMP → IGMP Group List tab

### 5.3.20 Configuring SNMP

SNMP → SNMP

SNMP (Simple Network Management Protocol) – is a protocol used to manage and monitor network devices. Using the SNMP protocol, the software can access information that is stored on managed devices (for example, on a switch). On managed devices, SNMP stores information about the device on which it operates in a database called MIB.

The switch supports SNMP v1 and SNMP v3.

#### 5.3.20.1 Configuring SNMP v1

Figure 5.3.20.1 Configuring SNMP v1

- State — state.

- Traps Server IP address – the IP address of the server to which SNMP Traps are sent.

- Version – SNMP protocol version.

- Read Community – read-only community, the string used for authentication in SNMP v1.  Also, Read Community is used to send SNMP Taps.

- Write Community – community for recording, the string used for authentication in SNMP v1. 

SNMP Traps will be sent only when events occur that are specified in the Event List tab

#### 5.3.20.2 Configuring SNMP v3

SNMP v3 provides a higher level of security compared to SNMP v1.

Fig. 5.3.20.2 Configuring SNMP v3

To configure SNMP v3, set the Version switch to "SNMP v3".

SNMP v3 allows to flexibly configure the security level.

The level is selected by the "Security Level" switch:

- NoAuth, NoPriv – authorization only on the User Name line, without encryption (this mode is similar to SNMP v1)

- Auth, NoPriv – Auth Password authentication (method HMAC-MD5-96), without encryption.

- Auth, Priv – Auth Password authentication (method HMAC-MD5-96), AES-128 encryption using the Priv Password key.

Engine ID – identifier in SNMP v3. For each Switch Engine ID is unique, it is generated based on the MAC address of the device. That is, you do not need to change it, but you can set your own value if necessary.

### 5.3.21 MAC address filtering

Security → MAC Address Filtering

TFortis switches support MAC address filtering for ports.

Figure 5.3.21.1 Configuring the port operating mode

In Normal state, the port operates in normal mode, performing packet switching as usual, allowing any MAC addresses.

When the port is switched to Secure state, only MAC address added manually to MAC Address Table can access this port. There are also several options how the port reacts to an unauthorized MAC address:

- Secure: MAC Filtration – if an unauthorized MAC address is detected on the port, only this MAC address is blocked and the port continues to operate.

- Secure: Port shutdown 2 if an unauthorized MAC is detected on the port, the port is blocked, data transmission stops.

- Secure: Temporary port shutdown – if an unauthorized MAC address is detected on the port, the port is blocked for 5 minutes, data transfer stops. After this timeout, the port switches back to transmit data. While unauthorized MAC remains the ports blocks again.

To add a new authorized MAC address, use Add New MAC Address table. In order to do so, provide a MAC address and a port number.

Figure 5.3.21.2 Adding a new MAC address and the MAC Address table.

#### 5.3.21.1 List of blocked MAC addresses

Security →Blocked MAC Address

When MAC address filtering is enabled, this table will show the MAC address of all the devices attempted to access one of the protected ports of the switch but were not listed as permitted for this port.

Figure 5.3.21.3  List of blocked MAC addresses

In order to inform the network administrators about access attempts from unknown MAC addresses, you need to set up this event. To do so, in section Events → Event List check the box MAC Filtering

Figure 5.3.21.4 Event setup

And then configure any logging protocol (Syslog, SNMP-Trap or SMTP)

### 5.3.22 Set up Camera Comfort Start

Special Functions → Comfort Start

Comfort Start – A safe start of the camera. The most problematic moment in camera operations is its start at low temperature. To ensure comfortable conditions for starting a camera in the cold season it is recommended to power on the heater of the thermal housing and only then turn on the camcorder. Checked box enables 1 or 2 hours delay between powering on the switch and turning on PoE for the camera.

Attention!

This function is available only for outdoor PSW switches

Attention!

This function requires TFortis TH-02 or TH-03 thermal housings

Soft start time – select the preheating duration. If the air temperature does not fall below minus 30°C, it is recommended to set the preheating to 1 hour, for lower temperatures, it is recommended to set it to 2 hours.

Manual start – forced camera start without waiting for the preheating cycle to finish.

Figure 5.3.22.1 Camera Comfort Start settings

### 5.3.23 Camera Hanging Control settings

Special Functions → Auto Restart

Attention!

This function is available only for outdoor PSW switches

This function aims to automatically restart the camera if it hangs. Restart is available only when the camera is powered by active PoE. Automatic restart is not available if the camera is powered by passive PoE or by third-party PoE injector.

Figure 5.3.23.1 Camera Auto Restart settings

Auto restart mode – hanging indicator.

There are tree indicators of hanging:

- Link- loss of Link camera signal.

- PING – no replies to service Ping requests.

- Speed — low port speed.

When using Ping indicator, provide camera IP address.

When using Speed indicator, set up minimum port speed threshold. Speed unit is Kbps.
Manual restart – camera forced restart.

### 5.3.24 Link Aggregation

Ports → Link Aggregation

This function is not implemented yet!

TFortis SWU switches support creation up to 5 aggregated links containing 2 to 8 ports. Aggregation of the switch physical ports into an aggregated channel allows to increase the throughput between switches by a factor of N (where N is the number of ports in the group) and to improve the fault tolerance of the system. Aggregation is static thus it requires the manual setup.

Figure 5.3.24.1 Creating aggregated channel

In order to aggregate port groups into an aggregated channel, you need to choose in the table Add Trunk aggregating ports and specify one of them as a master port.

- State – trunk state. Set Enable to activate.

- Master Port – master-port. Master port should belong to the list of ports selected to the port group.

- Add – add a new group.

When a new group is added, it appears in Trunk List.

Figure 5.3.24.2 List of aggregated channels

To finally apply settings, press Apply button.

### 5.3.25 Port Mirroring

Ports → Port Mirroring

SWU switch supports traffic mirroring from the specified ports to the target port.

Figure 5.3.25.1 Setup mirroring form port 2 to port 1

- State – enabling mirroring, by default mirroring is disabled.

- Target Port — target port that receives duplicate data from the source ports.

- Ports — source ports, the port supports several modes:

  - N (Normal) — the port operated in normal mode, mirroring is disabled.

  - R (Rx) – only received packets by this ports are duplicated to the target port

  - T (Tx) – only sent packets by this ports are duplicated to the target port

  - B (Both) – both, send and received packets of this port are duplicated to the target port

### 5.3.26 Events broadcasting to Teleport integration units

Special Function → Teleport

TFortis Teleport-1 integration unit is aimed at connecting TFortis PSW switches to the security systems.

One of the applications of Teleport-1 is the broadcasting of alarm events from TFortis PSW switches (opening the device casing, loss of connection to IP camera, etc.) to any security system, for example, "Bolid". The integration unit has relay outputs, to which the state of the dry contact inputs from the switch is relayed.

Figure 5.3.26.1 Network structure

Setup 	of the connection PSW switch ←→ Teleport integration unit requires the following steps:

1. Create the list of remote devices

Figure 5.3.26.2 Add new remote device

Name – text description, optional parameter, only for convenience

Type – the type of remote device (Teleport-1 or Teleport-2)

IP Address – IP address of the remote device

Added devices will be shown on the remote devices list:

Figure 5.3.26.3 Remote devices list

2. Binding the local input or event to the output of the remote device. Here you can bind, to which Teleport output the input signal is translated.

Figure 5.3.26.4 Inputs and events list

Inputs – input broadcasting settings

- Active – active. If this box is checked, the input is active and its state is broadcast to the remote device.

- Remote Device – remote device

- Remote Port – the remote device port number.

- Inverse – inverse input state. I.e. when the input is open, the output of the remote device will be short and vice versa.

- Current State – current input state.

Events – setting events broadcasting

- Active – active. If this box is checked, the event is broadcast to the remote device output.

- Remote Device – remote device

- Remote Port – the remote device port number.

- Inverse – inverse

- Current State – current state of the event

### 5.3.27 Cable Tester

Diagnostic Tools → Virtual Cable Tester

TFortis switches support the function of cable integrity check for "copper" Fast Ethernet ports. This test determines the type of fault (cutoff or short circuit) for each pair and specifies the distance from the switch to the fault location.

The physical principle of testing relies on the fact that the switch sends a test electrical impulse over the cable, and on the basis of the delay time and the phase of the received reflected signal determines the distance to the fault and its type.  For that period of time, the connection and the link on the tested port are intermitted.

If the cable is fault-free and the properly functioning network device is connected to the other side, it is not possible to measure cable length this way, because test signal will be terminated by the end device and will not be a reflection.

To start testing, press the button under the relevant port in Diagnostic section. In this case, after the test, the table will display the test results for pairs 1-2 (white-orange — orange) and 3-6 (white-green — green).

In addition, the SWU switches are testing pairs 4-5, 7-8.

Possible testing results:

- Short – Short circuit between pairs

- Open – Break or cable is not connected

- Good – there is no fault.

The guaranteed precision of cable length measurements by the tester is ± 2 meters. That is why it is possible that during the test of known good cable, the length of pairs 1-2 and 3-6 will be different. It may be attributed to the several factors: heterogeneous properties of copper conductors, different density of twisting of pairs, individual features of PSW switch.

In order to increase the accuracy of measurements, you can calibrate the cable tester.

To do so, connect the cable with a length of at least 2 meters (leaving the second end of the cable disconnected), in the Calibrate section of the WEB interface for the relevant port enter the length of the connected cable in meters in press Set. In this case, the test is carried out and the correction coefficient is calculated.

Figure 5.3.27.1 Cable Tester interface

### 5.3.28 Remote Ping

Diagnostic Tools → Ping

Figure 5.3.28.1 Remote PING interface

PING is a software utility used to test connection in TCP/IP-based networks. 
This utility sends four 32-bytes packages and waits for echo replies.

This utility helps you "ping" the camera directly from the switch. It may be useful to resolve problems.

### 5.3.29 Switch statistics

The switch provides a variety of statistic information that can be useful to solve network issues and for network administration.

#### 5.3.29.1 Port Statistics

Statistics → Port Statistics

Figure 5.3.29.1.1 Port Statistics

Statistics on received and sent data for each switch port.

- RX  – uncorrupted data received by the port (bytes).

- TX  – uncorrupted data sent from the port (bytes).

Note. All counters are 32-bit, they are reset after reaching the value 4294967295.

By pressing «More info» you can see more detailed statistics for a particular port (see Figure 5.3.24.1.2)

Figure 5.3.29.1.2 Detailed port statistics

#### 5.3.29.2 PoE Status

Statistics → PoE Status

Figure 5.3.29.2.1 PoE Status

This tab displays information on PoE injection and current power for each port. Status and power consumption are indicated only for active PoE.

Attention!

This function is available only for outdoor PoE PSW switches

- Status – PoE status (ON/OFF)

- Mode – power type: type A – the power is transmitted in pairs 1-2, 3-6. Type B – the power is transmitted in pairs 4-5, 7-8.

- Power – active PoE output power (W).

- Total Power – total power (W), for correct operation should not exceed the power budget.

#### 5.3.29.3 ARP Table

Statistics → ARP Table

The page contains the ARP cache of the switch processor, represented as a table.

Figure 5.3.29.3.1 ARP table

#### 5.3.29.4 MAC Table

Statistics → MAC Table

The tab contains the switching table: matching MAC-address to a physical port.

Figure 5.3.29.4.1 MAC table

#### 5.3.29.5 DNS Table

Statistics → DNS Table

This tab contains the output of the DNS protocol: matching hostname with its IP address.

Figure 5.3.29.5.1 DNS table

#### 5.3.29.6 System log

Statistics → Log

The tab contains switch log. There are 10000 entries per page, in order to navigate to the next page, click Next.

To save this log in a .txt file, press Download log as file.

Figure 5.3.29.6.1 Log

### 5.3.30 Firmware Update

Update/Backup → Update Firmware

PSW switch supports firmware update. The latest firmware is always available on website tfortis.ru/en.

To update the firmware, download the firmware archive file. Unpack. The firmware file has a *.img file extension.

Figure 5.3.30.1  *.img file

In web-interface go to Update Firmware tab and pick a firmware file by pressing the Browse button.

Figure 5.3.30.2  Press Browse

Figure 5.3.30.3  Pick a *.img file

Press the Upload button and wait until the file is copied into device internal storage.

Figure 5.3.30.4 Wait when the file upload is finished

When the file is uploaded, press Update to update or Cancel to cancel.

Figure 5.3.30.5  Press Update

After pressing Update, the update process will start. Do not reboot the switch or turn off the power.

Figure 5.3.30.6  Wait while firmware update process finishes

Note: the switch also supports updating via Telnet from an external TFTP server. For more information take a look at "Manage using Telnet" section.

### 5.3.31 Save and restore settings

Update/Backup → Backup/Recovery

PSW switches support saving current switch settings to a configuration file, this file editing and restoring settings from the file.

#### 5.3.31.1 Save settings to file

In the side menu, select Update/Backup → Backup/Recovery

Figure 5.3.31.1.1 Save and restore settings interface

In section 1 press the button «Download a file». You will be asked if you want to save or open the file, Save.

Figure 5.3.31.1.2 Saving the settings file

#### 5.3.31.2. Restore settings from the file.

If you want to restore previously saved settings from the file, then in  Update/Backup → Backup/Recovery tab, choose in section 2 (Recovery settings) *.bak configuration file and press «Upload» for upload.

Figure 5.3.31.2.1 Switch reboot

After uploading the file, the device will reboot and the settings will be applied.

#### 5.3.31.3 Editing configuration file

Changing the configuration file can be useful, when a group of devices has similar settings. In this case you can create a universal configuration file for these devices and change only a small set of parameters for each device, for example, the IP address. Other parameters will be taken from the configuration file.

The configuration file generated by the switch when saving settings to a file is a file with * .bak extension with settings in text form.

This file can be opened with any text editor.

The structure of the records has a strictly defined form of recording.  In general, it looks like this:

#<variable name>=[<variable value>]

Example: # IPADDRESS = [192.168.0.1], where the value of IPADDRESS variable is 192.168.0.1

Description of settings with default parameters is shown in Table 5.3.2.

Table 5.3.2. Configuration file variables

| Command syntax | Description |
| --- | --- |
| #IPADDRESS=[192.168.0.1] | IP address of the switch |
| #NETMASK=[255.255.255.0] | Subnet mask |
| #GATEWAY=[255.255.255.255] | default gateway |
| #USER_MAC=[c0:11:a6:0:0:0] | user's MAC address |
| #DNS=[255.255.255.255] | IP address of the DNS server |
| #DHCPMODE=[0] | DHCP mode (0 — disabled, 1 — DHCP client) |
| #LANG=[0] | interface language (0 – English, 1 — Russian) |
| #HTTP_USERNAME=[] #HTTP_PASSWD=[] | login and password for the default account (Admin access rights) |
| #USER1_USERNAME=[] | User name |
| #USER1_PASSWD=[] | Account password |
| #USER1_RULE=[0] | Access rights (0 – account disabled, 1 – Admin, 2 – User) |
| #SYSTEM_NAME=[] | device description |
| #SYSTEM_LOCATION=[] | device location |
| #SYSTEM_CONTACT=[] | contact information |
| #PORT1_STATE=[1] | port 1 state (1 – on / 0 – off) The same for other ports. |
| #PORT1_SPEEDDPLX=[0] | speed and duplex on port 1 (0 – auto, 1 – 10_half, 2 – 10_full, 3 – 100_half, 4 – 100_full, 5 – 1000_full), same for other ports. |
| #PORT1_FLOWCTRL=[0] | Flow Control on port 1 (0 – disable, 1 – enable), same for other ports. |
| #PORT1_WDT=[0] | automatic restart of the video camera connected to this port (0 – off, 1 –-restart after the loss of the Link signal, 2 – restart if no response to Ping, 3 – restart if speed is low), the same for other ports. |
| #PORT1_IPADDR=[0.0.0.0] | IP address of the camera connected to port 1, with the Ping restart function active, the same for other ports. |
| #PORT1_WDT_SPEED=[0] | The lower threshold of the speed on the port with the speed restart function active for port 1, the same for the other ports. In Kbps. |
| #PORT_SOFTSTART_TIME=[1] | preheating time for camera housings with comfort start function (1 – 1 hour, 2 – 2 hours) |
| #PORT1_SOFTSTART=[0] | comfort start function for port 1 (0 – enabled, 1 – disabled), the same for other ports. |
| #PORT1_POE=[257] | PoE control on port 1 (257 – enabled, 0 – disabled), the same for other ports. |
| #SFP1_MODE=[0] | The operating mode of the SFP1 port (0- forced, 1-auto), is the same for the SFP2 port. |
| #SMTP_STATE=[0] | SMTP protocol (0 – disabled, 1 — enabled) |
| #SMTP_SERV_IP=[0.0.0.0] | IP address of the SMTP server |
| #SMTP_TO1=[] | mailing address of recipient 1 |
| #SMTP_TO2=[] | mailing address of recipient 2 |
| #SMTP_TO3=[] | mailing address of recipient 3 |
| #SMTP_FROM=[] | mailing address of the sender |
| #SMTP_SUBJ=[TFortis PSW-2G4F] | e-mail subject |
| #SMTP_LOGIN=[] | login to access the mailbox |
| #SMTP_PASS=[] | password to access the mailbox |
| #SMTP_PORT=[25] | SMTP port |
| #SMTP_DOMAIN_NAME=[] | mail server domain name |
| #SNTP_STATE=[0] | SNTP protocol state |
| #SNTP_SETT_SERV=[0.0.0.0] | IP address of SNTP server |
| #SNTP_SERV_NAME=[] | Domain name of SNTP server |
| #SNTP_TIMEZONE=[0] | time zone, relative to UTC (from -12 to +13) |
| #SNTP_PERIOD=[10] | server synchronization period (1, 10 or 60 minutes) |
| #SYSLOG_STATE=[0] | Syslog protocol state |
| #SYSLOG_SERV_IP=[0.0.0.0] | IP address of the Syslog server |
| #EVENT_LIST_LINK_T=[12] | event of changing the link in the EventList (7 – disabled) |
| #EVENT_LIST_POE_T=[7] | event of changing the PoE status in the EventList list (7 – disabled) |
| #EVENT_LIST_STP_T=[7] | STP events in the EventList (7 – disabled) |
| #EVENT_LIST_ARLINK_T=[12] | event in the EventList (7 – disabled) |
| #EVENT_LIST_ARPING_T=[12] | event in the EventList (7 – disabled) |
| #EVENT_LIST_SYSTEM_T=[7] | event in the EventList (7 – disabled) |
| #EVENT_LIST_UPS_T=[12] | event in the EventList (7 – disabled) |
| #EVENT_LIST_ACCESS_T=[12] | event in the EventList (7 – disabled) |
| #EVENT_LIST_MAC_T=[12] | event in the EventList (7 – disabled) |
| #DRY_CONT0_STATE=[1] | tamper sensor active (for PSW-2G + and PSW-2G6F +) |
| #DRY_CONT1_STATE=[1] | dry contact 1 activation (0 – disabled, 1 – enabled) – Sensor 1 |
| #DRY_CONT1_LEVEL=[1] | alarm trip level for contact 1 (0 – by opening, 1 – by closing) |
| #DRY_CONT2_STATE=[1] | dry contact 2 activation (0 – disabled, 1 – enabled) |
| #DRY_CONT2_LEVEL=[1] | alarm trip level for contact 2 (0 – by opening, 1 – by closing) |
| #PORT1_RATE_LIMIT_RX=[0] | limiting the reception speed of port 1 in Kbps (0 – limit disabled), the same for other ports. |
| #PORT1_RATE_LIMIT_TX=[0] | limiting the transmission speed of port 1 in Kbps (0 – limit disabled) |
| #QOS_STATE=[0] | QoS state (0 – disabled, 1 — enabled) |
| #QOS_POLICY=[0] | scheduling mode (0 – weighted priority, 1 – strict priority) |
| #QOS_COS=[[1][0][0][1][2][2][3][3]] | matching CoS priority and service priority |
| #QOS_TOS=[[0][0][0][0][0][0][0][0][1][1][1][1][1][1][1][1][1][1][1][1][1][1][1][1][1][1][1][1][1][1][1][1][2][2][2][2][2][2][2][2][2][2][2][2][2][2][2][2][2][2][2][2][2][2][2][2][3][3][3][3][3][3][3][3]] | matching ToS priority and service queue |
| #PORT1_COS_STATE=[1] | activation of CoS on port 1, the same for other ports. |
| #PORT1_TOS_STATE=[1] | activation of ToS on port 1, the same for other ports. |
| #PORT1_QOS_RULE=[1] | selecting priority of CoS or ToS (0 – CoS has priority, 1 — ToS has priority), the same for other ports. |
| #PORT1_COS_PRI=[0] | priority by default for port 1, the same for other ports. |
| #VLAN_MVID=[1] | VID of the management VLAN |
| #VLAN_NUM=[1] | number of configured VLANs |
| #VLAN1=[[1][1][default][2][2][2][2][2][2][2][2][2][2]] | record with VLAN settings |
| #VLAN_TRUNK_STATE=[0] | VLAN Trunking (0 – disabled, 1 – enabled) |
| #VLAN_PORT1_STATE=[0] | Configuring port for VLAN Trunking (0 – VLAN Trunking on the port is disabled, 1 – enabled) |
| #STP_STATE=[0] | SMTP protocol activation (0 – disabled, 1 — enabled) |
| #STP_MAGIC=[65217] | always 65217 |
| #STP_PROTO=[2] | protocol (0 — STP, 2 – RSTP) |
| #STP_BRIDGE_PRIOR=[32768] | Bridge Priority |
| #STP_MAX_AGE=[20] | Bridge Max Age |
| #STP_HELLO_TIME=[2] | Bridge Hello Time |
| #STP_FORW_DELAY=[15] | Forward Delay Time |
| #STP_MIGRATE_DELAY=[3] | Migration Delay Time |
| #STP_TX_HCOUNT=[6] | TX Hold Count |
| #STP_PORT1_CFG=[[1][1][128][200000][10]] | record with port 1 settings, the same for other ports. |
| #BPDU_FORWARD=[1] | forwarding BPDU packets with STP / RSTP protocol disabled (0 – disabled, 1 –enabled) |
| #PORT1_VCT_ADJ=[100] | coefficient of correction by cable tester for port number 1, the same for other ports |
| #PORT1_VCT_LEN=[0] | length of the line for cable tester for port number 1, the same for other ports. |
| #SNMP_STATE=[0] | SNMP (0 – disabled, 1 — enabled) |
| #SNMP_SERVER=[0.0.0.0] | IP address of the SNMP Traps server |
| #SNMP_VERS=[0] | SNMP protocol version (0 – SNMP v1, 3– SNMP v3) |
| #SNMP_COMMUNITY1=[public] | reading community |
| #SNMP_COMMUNITY2=[private] | writing community |
| #SNMPV3_USER1_LEVEL=[0] | Security level (0 — NoAuth,NoPriv, 1 – Auth,NoPriv, 2 – Auth,Priv) |
| #SNMPV3_USER1_USER_NAME=[] | User name for SNMP v3 |
| #SNMPV3_USER1_AUTH_PASS=[] | Auth Password for SNMP v3 |
| #SNMPV3_USER1_PRIV_PASS=[] | Priv Password for SNMP v3 |
| #SNMP3_ENGINE_ID=[] | Engine ID for SNMP v3 |
| #IGMP_STATE=[0] | IGMP (0 – disabled, 1 – enabled) |
| #IGMP_QUERY_MODE=[1] | IGMP General Query sending (0 – disabled, 1 – enabled) |
| #IGMP_PORT_1_STATE=[1] | inclusion of port 1 in IGMP protocol, the same for other ports. |
| #IGMP_QUERY_INTERVAL=[60] | IGMP Query Interval |
| #IGMP_QUERY_RESP_INTERVAL=[10] | IGMP Query response Interval |
| #IGMP_GROUP_MEMB_TIME=[250] | Group Membership Time |
| #IGMP_OTHER_QUERIER_INTERVAL=[255] | Other Querier Interval |
| #TELNET_STATE=[1] | Telnet state (0 – disabled, 1 — enabled) |
| #TFTP_MODE=[0] | TFTP mode (0 – disabled, 1 — enabled) |
| #TFTP_PORT=[69] | UDP port on TFTP |
| #PLC_EM_MODEL=[0] | Energy meter model |
| #PLC_EM_BAUDRATE=[5] | Speed of port RS485 (0 – 300, 1 – 600, 2 – 1200, 3 – 2400, 4 – 4800, 5 – 9600, 6 – 19200) |
| #PLC_EM_PARITY=[0] | RS485 parity (0 – Disable, 1 – Even, 2 – Odd) |
| #PLC_EM_DATABITS=[8] | Number of data bits |
| #PLC_EM_STOPBITS=[1] | Number of stop bits |
| #PLC_EM_PASS=[] | Identifier (login) to connect to the energy meter |
| #PLC_EM_ID=[] | Password to connect to the enegry meter |
| #PLC_OUT1_STATE=[0] | State of output 1 for the expansion board (0-short, 1-open, 2-logic) |
| #PLC_OUT1_ACTION=[0] | Action for output 1 when the logic condition is met (0-short, 1-open, 2-impulse) |
| #PLC_OUT1_EVENT1=[0] | Event 1 for output 1 of the expansion board |
| #PORT1_MACFILT=[0] | Enabling MAC address filtering on port 1 (0-Normal, 1-Secure: Mac Filtration, 2-Secure: Port shutdown, 3-Secure: Temporary port shutdown) |
| #MAC_BIND_ENRTY1_ACTIVE=[0] | Record 1 in the table of allowed MAC addresses (1-record is active) |
| #MAC_BIND_ENRTY1_MAC=[0:0:0:0:0:0] | Record 1 in the table of allowed MAC addresses (MAC address) |
| #MAC_BIND_ENRTY1_PORT=[0] | Record 1 in the table of allowed MAC addresses (Port number) |

### 5.3.32 Reset to factory settings

Reboot/Default → Factory Default

Figure 5.3.32.1 Resetting the switch

If necessary, it is possible to reset the settings to the factory settings. The resetting can be selective:

Keep current Network settings — Reset all settings, but keep current network settings: IP, MAC, Gateway, Mask
	Keep current username & password — Reset all settings, but keep current access settings: Username, Password
	Keep STP settings — Reset all settings, but keep current STP/RSTP settings.

### 5.3.33 Reboot

Reboot/Default → Reboot

If necessary, the switch can be remotely rebooted.

There are two reboot options:

- Reboot CPU – Rebooting the processor only.

- Reboot All – Complete reboot (processor, PoE, switching part)

Figure 5.3.33.1 Switch reboot

### 5.3.34 Optional expansion board

Depending on the package, TFortis PSW outdoor switches can be equipped with an additional expansion board that increases the functionality of the device.

At the moment, TFortis switches can be equipped with one of the following two versions of the board: PLC-01 and PLC-02.

PLC-01 expansion board has the following interfaces:

- 2 relay outputs (250V, 10A)

- 1 RS485 output to connect to power metering devices.

PLC-02 expansion board has the following interfaces:

- 3 dry contact inputs

- 1 relay output (250V, 100mA)

- 1 RS485 output to connect to power metering devices.

#### 5.3.34.1 Digital inputs

Special Function → Inputs/Outputs

Depending on the expansion board model, it can be equipped with dry contact digital inputs. The inputs can be used to connect various sensors to detect a short circuit or an opening, for example, a tamper sensor, a motion sensor, etc.

For each input, you can configure an alarm condition, in which a message will be sent to the server.

Figure 5.3.34.1 Configuring inputs

- Enable – enables input operation. To send messages about changing of the input state, set to Enable. A message will be sent, if State is set to Enable, and Current State matches Alarm State and a tick is set in Inputs/Outputs in the Events List tab.

If Disable is present, changing the input state will not trigger events.

- Alarm State – the state of the input that is considered an alarm (Open – open state, Short – closed state, Any Change – the event is generated in case of any input change).

- Current State – current input state.

#### 5.3.34.2 Relay outputs

Special Function → Inputs/Outputs

The expansion board may have 1 or 2 relay outputs

Attention: PLC-02 relay output is low-current, use external relay elements to connect a powerful load.

Figure 5.3.34.2 Configuring the relay output

For each output, you can set the Initial State, that is, the state of the output immediately after the switch is turned on.

#### 5.3.34.3 Logic

Special Function → Inputs/Outputs

The switch can operate as a simple logic controller. A certain output behavior can be set for the inputs triggering.

Event is the event in which the condition is triggered. Check boxes to select the list of events that will affect the output. If at least one of the selected events is executed (the rule of logical "OR" is valid), the relay output is transferred to the Action state. If none of the events occur, the output is in the inverse state.

The Action state can be:

- Open – relay outputs are open

- Short – relay outputs are closed

- Impulse – relay outputs change their state to inverse for 10 seconds, then switch back to the initial state.

Let's see an example:

When the inputs of Sensor 1 and Input 1 are closed, an event occurs.

Figure 5.3.34.3 Configuring logic

It is necessary that the relay, which is normally closed, opens when an event occurs. Set the Initial State to Short (closed) and select the event sources (Sensor 1 and Input 1) and the output state (Action)

Figure 5.3.34.4 Configuring logic

#### 5.3.34.4 RS485 output

Special Function → RS-485

The expansion board has a built-in RS485 output, intended for connecting additional devices via the RS485 interface. At the moment, only metering devices are supported. Before connecting a remote device, it is necessary to configure the interface.

Figure 5.3.34.5 Configuring RS485

#### 5.3.34.5 Connecting energy meters

TFortis switch has a function to obtain readings from the energy meter via the RS485 interface with the expansion board connected.

Procedure of connecting to the energy meter:

- Electrical connection

- Interface configuration (speed, number of data bits, etc.)

- Selecting the energy meter model, connection to the meter to obtain readings about total consumption and power costs based on one of 4 tariffs.

Note: the following models are supported at the moment:

- Energomera СЕ102М

Configuring connection to the energy meter

Figure 5.3.34.6 Configuring connection to the energy meter

To configure the device, fill in the following fields:

- Model – energy meter model

- Identification – device ID

- Password – access password

If the device ID and the access password are not specified, the interaction with the energy meter will occur without password (if allowed by the settings of the energy meter).

After connection, the following information will be available:

Figure 5.3.34.7 Readings received

- Model – energy meter model

- State – state of connection, result of reading data

- Total indications – total power consumption indications

- T1, T2, T3, T4 – indications by tariff

## 5.4 Management via Telnet

Telnet is used for remote management of network equipment through the command line. Telnet uses TCP protocol and port 23.

In TFortis switches, Telnet is enabled by default. If necessary, you may disable it: go to Basic Settings → Telnet

Figure 5.4.1 Configuring Telnet

Telnet supports the following extra modes:

1. Short commands. It is possible to work with short commands (you do not need to enter the command to the end).

Example: if you need to enter the command config ports 1-2 state enable, you can reduce it to the minimum: co po 1-2 st en

2. Auto-completion of commands. The ability to press the TAB key to complete the command entered.

Example: If you enter con and press TAB, the command will complete to config

3. Command history. The history of the entered commands is available. Switching is done with the UP, DOWN keys

You can connect to the device using any terminal program. In this document, the configuration will be based on the example of Microsoft Telnet. Connect using the command "open <IP address>"

After connection it is required to enter login and password. Login and password for Telnet are the same as for accessing the WEB interface. If the login and password are not set, press Enter twice.

Note: if login / password were entered incorrectly 30 times in a row, access to Telnet is blocked for 1 hour.

The # symbol and the device name indicate that the authentication was successful and the switch went into configuration mode. (Access rights – Admin)

If you have entered the login / password for an account with limited rights, you will enter the viewing mode. (Access rights – User)

The list of commands can be obtained using the command "?" or "help"

The following designations are used as command arguments:

- <IP> – IP address in XX.XX.XX.XX format

- <STATE> – state, either enable or disable

- <VALUE> – any signed or unsigned integer

- <STRING> – text line

- <PORTLIST> – list of ports as follows: initial_port-terminal_port, or port.

Example: For ports 1, 2, 3: "1-3" ; only for port 2: "2"

Setting process via Telnet includes several steps:

- Using the subset of commands from the config group, the required configuration is set.

- This configuration is saved into memory with the save command, after which the settings are applied

Attention:

If after setting the parameters the device is rebooted without using the save command, the settings will not be saved.

### 5.4.1 Example of setting

Let's look at the process of switch configuring.

For example, we need to set the following settings:

- IP address 192.168.0.100

- Gateway 192.168.0.1

- We will add VLAN 2 with a tagged Gigabit Ethernet 1 port (Port 5) and an untagged Fast Ethernet 1 port (Port 1)

- Set up a comfort start on the Fast Ethernet port 1 (Port 1)

- Configure the automatic reset of the hanging cameras on port 1 by the PING criterion (IP address 192.168.0.13)

- Enable the RSTP protocol by the default settings

Now let's connect to the device. If the device has not yet been configured, then its IP address 192.168.0.1, login and password for access are not specified.

Let's go to the management mode

Change the IP address by the command config ipif System ipaddress 192.168.0.100

Add a default gateway: config ipif System gateway 192.168.0.100

Add VLAN 2.

To do that, first exclude port 1 from VLAN 1

Make port GE1 (port 5) in VLAN 1 tagged

Now add un untagged port 1 to VLAN 2

Add a tagged port 5 to VLAN 2

Use the command show vlan to check proper configuration:

Now let's activate the comfort start function for port 1

We will configure protection against camera hanging on the same port (192.168.0.13) by the PING criterion

Now let's proceed to RSTP setting. Since we decided to use the default parameters, we only need to enable the protocol and select the version.

Now the setup is complete, let's save the settings

### 5.4.2 Description of Telnet commands

The switches support the following set of Telnet commands:

1. The config command group:

- ipif – network settings (IP address, subnet mask, gateway)

- ports – ports settings (speed, duplex, PoE)

- igmp_snooping – IGMP setting

- stp – STP/RSTP setting

- snmp – SNMP setting

- syslog – Syslog setting

- vlan – VLAN setting

- sntp – SNTP setting

- smtp – SMTP setting

- comfortstart — setting the function of cameras comfort start

- autorestart – configuring the function of camera hanging control

- dry_cont – configuring dry contacts

- user_account – setting user name / password

- tftp — TFTP setting

- events – events setting

- 802.1p — QoS setting

- scheduling_mechanism — scheduling mode in QoS

- dscp_mapping – setting the priority of DSCP in QoS

- bandwidth_control – setting the port speed limit

- description – specify the description of the device

- mac_filtering – MAC address filtering

- inputs – setting the inputs of the expansion board

- outputs – setting the outputs of the expansion board

- rs485 – setting RS485

- aggregation – setting aggregated channels (for TFortis SWU)

- mirroring – setting mirroring (for TFortis SWU)

- teleport –configuring transmitting of inputs and events to Teleport integration units

2. The show command group

- switch — summary information about the device

- ports — information about ports

- igmp_snooping — information about IGMP Snooping operation

- stp — information about STP/RSTP protocols

- snmp — information about SNMP

- syslog – information about SYSLOG protocol

- vlan – information about configured VLANs

- sntp — information about SNTP

- smtp — information about SMTP

- firmware — information about current firmware version

- packet — statistics on the transmitted / received packets on the port

- fdb — switching table

- arpentry — ARP table of the switch

- autorestart — information about Autorestart function

- comfortstart — information about Comfortstart function

- dry_cont – information about the state of dry contacts

- tftp — information about TFTP

- events – information about configured events

- 802.1p — information about basic QoS settings

- scheduling_mechanism — scheduling mode in QoS

- dscp_mapping — distribution of DSCP labels by queues in QoS

- bandwidth_control – information about limitation of speed on the port

- poe – information about PoE

- config – displays the entire switch configuration

- mac_filtering – information about MAC address filtering

- inputs – information about the inputs of the expansion board

- outputs – information about the outputs of the expansion board

- rs485 – RS485 configuration information

- aggregation – information about setting up aggregated channels

- mirroring – information about configuring port mirroring

- teleport – information about setting up the broadcast to Teleport integration units

3. Firmware upgrade and configuration download from TFTP server

download

4. Save settings and system log to TFTP server

upload

5. Ping utility

ping

6. Virtual Cable testing utility (Cable tester)

cable_diag

7. Save and apply settings

save

8. Reboot

reboot

9. Display help on commands

help or ?

10. Exit Telnet management mode

exit

### 5.4.3 The config group

#### 5.4.3.1 Network settings (config ipif)

1. IP address of the switch

config ipif System ipaddress <IP>

Example: config ipif System ipaddress 192.168.0.100

2. Subnet mask of the switch.

config ipif System netmask <IP>

Example: config ipif System netmask 255.255.255.0

3. Gateway address

config ipif System gateway <IP>

Example: config ipif System gateway  192.168.0.1

4. Address of the DNS server

config ipif System dns <IP>

Example: config ipif System dns  192.168.0.1

5. DHCP client mode

config ipif System dhcp <STATE>

Example: config ipif System dhcp enable – DHCP client mode enabled

#### 5.4.3.2 Configuring ports (config ports)

1. Port state (the port may be forced to disable)

config ports <PORTLIST> state <STATE>

Example: config ports 1-1 state disable

2. Speed on the port

config ports <PORTLIST> speed <SPEED>

<SPEED> make take the following values

- auto

- 100_full

- 100_half

- 10_full

- 10_half

Example: config ports 1-6 speed auto

3. Flow Control

config ports <PORTLIST> flow_control <STATE>

Example:  config ports 1-2 flow_control enable

4. PoE management (Power over Ethernet)

config ports <PORTLIST> poe <STATE>

Example:  config ports 1-1 poe disable

5. SFP port mode (only for ports with SFP slot)

config ports <PORTLIST> sfp_mode  <SMODE>

<SMODE> may take the following values

- auto – compatibility with CISCO and some other equipment

- forced – main mode compatible with the majority of equipment. Forcing the link to come up when an optical signal is detected

Example:  config ports 6-6  sfp_mode auto

#### 5.4.3.3 Configuring multicast (IGMP Snooping)

1. Enable IGMP Snooping

config igmp_snooping state <STATE>

Example:  config igmp_snooping state enable

2. List of ports with active snooping

config igmp_snooping portlist <PORTLIST>

Example:  config igmp_snooping portlist 1-6

3. Query Interval – time interval between sending messages 	Query (in seconds)

config igmp_snooping query_interval <VALUE>

Example: config igmp_snooping query_interval  60

4. Query Response Interval – maximum response time from 	the host for sending periodic public messages from Query (1-25 seconds)

config igmp_snooping query_response_interval <VALUE>

Example: config igmp_snooping query_response_interval  10

5. Group Membership Interval – time interval when 	the router waits for getting IGMP Report (1-255 seconds)

config igmp_snooping group_membership_time <VALUE>

Example: config igmp_snooping group_membership_time 255

6. Other Querier Present Interval – if the switch is Non-Querier, then if 	it has not received a Query during this interval, it starts to consider itself	 	a Querier.

config igmp_snooping other_querier_present_int <VALUE>

Example: config igmp_snooping other_querier_present_int 255

7. Send IGMP Query – disable sending 	General Query messages by the switch

config igmp_snooping send_query <STATE>

Example: config igmp_snooping send_query disable

#### 5.4.3.4 Configuring STP/RSTP

1. Enable STP/RSTP

config stp state <STATE>

Example: config stp state enable

2. Selecting protocol version STP or RSTP

config stp version <VERSION>

<VERSION> make take the following values

    - stp

    - rstp

Example:  config stp version rstp

3. Bridge priority

config stp priority <VALUE>

Example: config stp priority 32768

4. Bridge Hello Time

config stp hellotime <VALUE>

Example: config stp hellotime 2

5. TX Hold Count

config stp txholdcount <VALUE>

Example:  config stp txholdcount 6

6. Bridge Max Age

config stp maxage <VALUE>

Example:  config stp maxage 20

7. Forward Delay Time

config stp forwarddelay <VALUE>

Example:  config stp forwarddelay 15

8. Enable BPDU Forwarding

config stp forward_bpdu state <STATE>

Example: config stp forward_bpdu state enable

#### 5.4.3.5 Configuring SNMP

1. Enable SNMP

config snmp state <STATE>

Example:  config snmp state enable

2. IP address of the server (for SNMP Traps)

config snmp host <IP>

Example:  config snmp host 192.168.0.1

3. Read Community string

config snmp read_community <STRING>

Example:  config snmp read_community public

4.Write Community string

config snmp write_community <STRING>

Example:  config snmp write_community private

5. Protocol version (SNMPv1 and SNMPv3 are supported)

config snmp version <VALUE>

where <VALUE> is:  1, 3

Example:  config snmp version 1

6. Security Level for SNMP v3

config snmp level <VALUE>

where <VALUE> is:

0 –  NoAuth, NoPriv

1 – Auth, NoPriv

2 – Auth, Priv

Example:  config snmp level 2

7. User name for SNMP v3

config snmp user_name <STRING>

Example:  config snmp user_name administrator

8. Auth Password  for SNMP v3 (required is the selected security level is 	Auth,NoPriv or Auth,Priv)

config snmp auth_pass <STRING>

Example:  config snmp auth_pass test

9. Priv Password for SNMP v3 (required if the selected security level is 	Auth,Priv)

config snmp priv_pass <STRING>

Example:  config snmp priv_pass test

9. Engine ID for SNMP v3, unique identifier

config snmp engine_id <STRING>

Example:  config snmp engine_id  8000A42303C011A6050001

#### 5.4.3.6 Configuring Syslog

1. Enable Syslog

config syslog state <STATE>

Example: config syslog state enable

2. IP address of the server

config syslog host <IP>

Example: config syslog host 192.168.0.1

#### 5.4.3.7 Configuring VLAN

1. Adding and editing VLAN

1.1 Adding and editing tagged ports in VLAN

config vlan vlanid <VALUE> add tagged <PORTLIST>

<VALUE> – VLAN ID for editing

<PORTLIST> – list of ports to which it is applicable

Example: config vlan vlanid 1 add tagged 1-3

1.2 Adding and editing untagged ports

config vlan vlanid <VALUE> add untagged <PORTLIST>

<VALUE> – VLAN ID for editing

<PORTLIST> – list of ports to which it is applicable

Example: config vlan vlanid 1 add untagged 4-4

1.3 Adding and editing ports not belonging to the VLAN

config vlan vlanid <VALUE> add not_memb <PORTLIST>

<VALUE> – VLAN ID for editing

<PORTLIST> – list of ports to which it is applicable

Example: config vlan vlanid 1 add not_memb 5-6

2. Deleting a VLAN

config vlan vlanid <VALUE>  delete vlan

Example: config vlan vlanid 2 delete

3. Renaming VLAN

config vlan vlanid <VALUE>  name <STRING>

Example: config vlan vlanid 2 name my_vlan2

Renaming VLAN with VID 2 to "my_vlan2"

4. Configuring Management VLAN

config vlan mngt_vlan <VALUE>

Example: config vlan mngt_vlan 2

Change VLAN to 2

5. Configuring VLAN Trunking

5.1 Enable VLAN Trunking

config vlan vlan_trunking state <STATE>

Example:   config vlan vlan_trunking state enable

5.1 Configuring ports in VLAN Trunking

config vlan vlan_trunking ports <PORTLIST> state <STATE>

Example:   config vlan vlan_trunking ports 1-2 state enable

#### 5.4.3.8 Configuring SNTP

1. Enable SNTP

config sntp state <STATE>

Example: config sntp state enable

2. IP address of SNTP server

config sntp primary <IP>

Example: config sntp primary 192.168.0.1

3. Time zone (relative to UTC)

config sntp timezone <VALUE>

Example: config sntp timezone +6

#### 5.4.3.9 Setting the comfort start function for the cameras

1. Camera housing preheating time (1 or 2 hours)

config comfortstart sstime <VALUE>

Example: config comfortstart sstime 2

2. Enable function on the ports

config comfortstart portlist <PORTLIST> state <STATE>

Example: config comfortstart portlist 1-4 state enable

#### 5.4.3.10 Setting protection from hanging

1. Enable function on the ports

config autorestart port <PORTLIST> state <AR_STATE>

where <AR_STATE> may take the following values:

- disable

- link

- ping

- speed

Example: config autorestart port 1-4 state link

2. IP cameras on the port (if control by PING is selected)

config autorestart port <PORTLIST> host <IP>

Example: config autorestart port 1-1 host 192.168.0.13

3. Minimum speed on the port (if Speed is slected) in Kbps.

config autorestart port <PORTLIST> min_speed <VALUE>

Example: config autorestart port 1-1 min_speed 3

#### 5.4.3.11 Configuring dry contacts (digital inputs)

There are inputs in the command system with ordinal numbers 0-2.

- Input 0 – tamper sensor on the cover of TFortis PSW-2G + and TFortis PSW-2G6F + switches.  Input trigger level cannot be changed.

- Input 1 – main input used to connect user sensors, it is marked "Sensor 1" of the switch board

- Input 2 – an additional input, can also be used to connect sensors, but does not have protection, like Input 1, marked "Sensor 2" on the switch board.

In general, the following commands are applicable for inputs:

1. Enable input operation (i.e., triggering an input causes 	an event to occur that can be sent in a specified way, 	for example, Syslog)

config dry_cont <NUM> state <STATE>

where:

<NUM> – input number

<STATE> – state

Example: config dry_cont 1 state enable

2. Selecting an input state that is considered an alarm and 	an event is generated

config dry_cont <NUM> alarm_level <STATE>

where:

<NUM> – input number (0-2)

<STATE> – a state that is considered an alarm:

- short – cloased state

- open — open state

Example: config dry_cont 1 alarm_level connected

#### 5.4.3.12 Configuring TFTP

1. Enable TFTP

config tftp state <STATE>

Example: config tftp state enable

2. configuring UDP port (by default port 69)

config tftp port <NUM>

Example: config config tftp port 69

#### 5.4.3.13 Configuring events

It is necessary to configure events that will be sent to the monitoring 	server. If Syslog protocol is used, 	it is also necessary to indicate event significance.

<STATE> variable takes the value enable/disable

<NUM> variable shows the significance level 0..7

1. changing link status

config events port_link state <STATE> level <NUM>

Example: config events port_link state enable level 4

2. changing PoE status

config events port_poe	state <STATE> level <NUM>

Example: config events port_poe state enable level 4

3. changing topology in STP/RSTP protocols

config events stp	state <STATE> level <NUM>

Example: config events stp state enable level 4

4. lost link with Auto Restart active

config events ar_link state <STATE> level <NUM>

Example: config events ar_link state enable level 4

5. remote device did not respond to PING with the Auto Restart function active 	AutoRestart

config events ar_ping state <STATE> level <NUM>

Example: config events ar_ping state enable level 4

6. low steed on the port with AutoRestart active

config events ar_speed state <STATE> level <NUM>

Example: config events ar_speed state enable level 4

7. low speed on the port with AutoRestart active

config events ar_speed state <STATE> level <NUM>

Example: config events ar_speed state enable level 4

8. system events

config events system state <STATE> level <NUM>

Example: config events system state enable level 4

9. UPS events

config events ups state <STATE> level <NUM>

Example: config events ups state enable level 4

10. dry contacts activation

config events dry_cont state <STATE> level <NUM>

Example: config events dry_cont state enable level 4

#### 5.4.3.14 Configuring user accounts

1. Creating a new account

config user_account add <USERNAME> <PASSWORD> <MODE>

where  <USERNAME>  is the user name (maximum 20 characters),

<PASSWORD> is the password (maximum 20 characters),

<MODE> is the access rights level:

- admin_rule

- user_rule

Example: config user_account add username password admin_rule

Create an administrator account with  username "username" and password 	"password"

2. Editing user data

config user_account add <USERNAME> <PASSWORD> <MODE>

where  <USERNAME>  is the user name (maximum 20 characters),

<PASSWORD> is the password (maximum 20 characters),

<MODE> is the access rights level:

- admin_rule

- user_rule

Example: config user_account add username password user_rule

"Username" account has different access rights now (	User)

3. Delete a user

config user_account delete <USERNAME>

where  <USERNAME>  is the user name (maximum 20 characters)

Example: config user_account delete username

Account "username" has been deleted.

#### 5.4.3.15 Configuring QoS

1. Enable QoS

config 802.1p state <STATE>

Example: config 802.1p state enable

2. Configuring Default priority

config 802.1p default_priority ports <PORTLIST>  <NUM>

where <NUM> is priority 0-7

Example: config 802.1p default_priority ports 1-3 7

3. Configuring CoS priority

config 802.1p user_priority <NUM1> <NUM2>

where <NUM1> is priority number (0-7),

<NUM2> is the number of queue serving this priority (0-3)

Example: config 802.1p user_priority 5 2

4. scheduling mode

config scheduling_mechanism <MODE>

where <MODE> is:

- strict – Strict priority – packets with high priority will be processed first

- weight_fair – Weighted fair priority – packets with different priority are processed by the switch with the ratio 8: 4: 2: 1

5. Configuring ToS priorities (DSCP)

config dscp_mapping dscp_value <NUM1> queue <NUM2>

where <NUM1> is the value of DSCP label 0-63,

<NUM2> is the number of queue serving this priority (0-3)

Example: config dscp_mapping dscp_value 61 queue 3

6. Configuring speed limits on the ports

config bandwidth_control <PORT_LIST> <MODE> <NUM>

where <PORT_LIST> is the list of ports,

<MODE>  is the limit direction:

- rx_rate — reception limit

- tx_rate — transfer limit

<NUM> is the speed value in Kbps, 0 – no limit.

5.4.3.16 Configuring device description

1. configuring device name

config description name <STRING>

Example:  config description name psw-2g4f

2. configuring device location

config description location <STRING>

Example:  config description location servernaya

3. configuring contacts of the service company

config description location <STRING>

Example:  config description company superpuper-telecom

#### 5.4.3.17 Configuring MAC address filtering

1. Configuring port state

config mac_filtering port_state <PORTLIST>  <MODE>

where <PORT_LIST> is the list of ports,

<MODE> is port mode:

- normal – Normal

- mac – Secure: MAC Filtering

- port – Secure: Port Shutdown

- port_temp – Secure: Temporary Port Shutdown

Example: config mac_filtering port_state 1-3 mac

2. Adding a MAC address to the allowed list

config mac_filtering add <PORT>  <MAC>

where <PORT> is port,

<MAC> is MAC address

Example: config mac_filtering add 1 00:11:22:33:44:55

3. Deleting a MAC address from the list of allowed

config mac_filtering del <PORT>  <MAC>

where <PORT> is port,

<MAC> is MAC address

Example: config mac_filtering del 1 00:11:22:33:44:55

#### 5.4.3.18 Configuring inputs of the expansion board

1. Enable input

config inputs <INPUT> state <STATE>

where <INPUT> is the input number,

<STATE> is the input state:

- enable – input active

- disable — input inactive

Example: config inputs 1 state enable

2. Configuring an alarm state

config inputs <INPUT> alarm_level <STATE>

where <INPUT> is the input number,

<STATE> is the port state when an event occurs

- open – open

- short — closed

- any – any change in the state

Example: config inputs 1 alarm_level short

#### 5.4.3.19 Configuring outputs of the expansion board

1. Configuring initial output state

config outputs  <OUTPUT> state <STATE>

where <OUTPUT> is the output number,

<STATE> is the output state:

- short — closed

- open – open

- logic — logic

Example: config outputs 1 state logic

2. Configuring a list of events for the output

config outputs  <OUTPUT> events <EVENTS>

where <OUTPUT> is the output number,

<EVENTS> is the list of events when the port changes its state

- sensor1 – dry contact 1

- sensor2 — dry contact 2

- input1 — input 1

- input2 — input 2

- input3 — input 3

Several events may be specified for one input

Example: config outputs 1 events sensor1 input1 input3

3. Configuring actions for the output when an event occurs

config outputs  <OUTPUT> action <STATE>

where <OUTPUT> is the output number,

<STATE> is the output state it will take when an event occurs

- open – open

- short — closed

- impulse — impulse (duration 10 seconds)

Example: config outputs 1 action short

#### 5.4.3.20 Configuring RS485

1. Port speed

config rs485  baudrate <BR>

where <BR> is the speed, selected from 300, 600, 1200, 2400, 4800, 9600, 	19200

Example: config rs485 baudrate 9600

2. Checking parity

config rs485  parity <PARITY>

where <PARITY> is parity check

- disable – checking disabled

- even — even

- odd — odd

Example: config rs485 parity even

3. Number of data bits

config rs485  databits <DATABITS>

where <DATABITS> is the number of data bits

Example: config rs485 databits 7

4. Number of stop bits

config rs485  stopbits <STOPBITS>

where <STOPBITS> is the number of stop bits

Example: config rs485 databits 1

5. Selecting energy meter model

config rs485  model  <NUM>

where <NUM> is the model number (1 — Energomera CE102M)

Example: config rs485 model 1

6. Configuring idenifier

config rs485  identification  <STRING>

where <STRING> is the identifier

Example: config rs485  identification www.energomera.ru

6. Setting password

config rs485  password  <STRING>

where <STRING> is the identifier

Example: config rs485  password 777777

#### 5.4.3.21 Configuring channel aggregation

This function is only supported by TFortis SWU switches

1. Creating a new group of aggregated ports

config aggregation add <NUM>

where <NUM> is the entry number (1..5)

Example: config aggregation add 1

2. Deleting a group of aggregated ports

config aggregation del <NUM>

where <NUM> is the number of the existing entry (1..5)

Example: config aggregation del 1

3.1  Active state of the group

config aggregation trunk  <NUM> state <STATE>

where <NUM>is the entry number (1..5)

<STATE> is state of the group

- enable — group is active

- disable — group is inactive

Example: config aggregation trunk 1 state enable

3.2 Configuring master port of the group

config aggregation trunk  <NUM> master <PORTLIST>

where <NUM>is the entry number (1..5)

<PORTLIST> is the number of master port

Example: config aggregation trunk 1 master 14

  - Configuringmember ports of the group

config aggregation trunk  <NUM> ports <PORTLIST>

where <NUM>is the entry number (1..5)

<PORTLIST> is port numbers

Example: config aggregation trunk 1 ports 10-15

#### 5.4.3.22 Configuring port mirroring

This function is only supported by TFortis SWU switches.

1. Enable mirroring

config mirroring state <STATE>

where <STATE> is protocol state

- enable — mirroring enabled

- disable — mirroring disabled

Example: config aggregation trunk 1 state enable

### 5.4.4 Show group

Possible commands:

- switch — summary information about the device

- ports — information about ports

- igmp_snooping — information about IGMP Snooping operation

- stp — information about STP/RSTP protocols

- snmp — information about SNMP

- syslog – information about SYSLOG protocol

- vlan – information about configured VLANs

- sntp — information about SNTP

- smtp — information about SMTP

- firmware — information about current firmware version

- packet — statistics on the transmitted / received packets on the port

- fdb — switching table

- arpentry — ARP table of the switch

- autorestart — information about Autorestart function

- comfortstart — information about Comfortstart function

- dry_cont – information about the state of dry contacts

- tftp — information about TFTP

- events – information about configured events

- 802.1p — information about basic QoS settings

- scheduling_mechanism — scheduling mode in QoS

- dscp_mapping — distribution of DSCP labels by queues in QoS

- bandwidth_control – information about limitation of speed on the port

- poe – information about PoE on all ports

- config – viewing full configuration

- mac_filtering – information about MAC address filtering

- inputs – information about the inputs of the expansion board

- outputs – information about the outputs of the expansion board

- rs485 – RS485 configuration information

All commands in this group can be divided into several subgroups:

- Viewing information about the switch (This includes variables such as port statistics, ARP table, firmware version, up-time)

- Viewing switch settings (View current switch settings)

#### 5.4.4.1 View switch information

1. Display full information about the device and its configuration

show switch

2. Display information about ports (state, link, speed, duplex  	PoE)

show ports – for all ports

show ports <PORTLIST> – only for ports in the list

3. Display information about integrated firmware 	of the switch

show firmware

4. Display switching tables (FDB)

show fdb

5. Display MAC tables

show arpentry

6. Display statistics about data transmitted/received by ports (incoming / outgoing packets)

show packet — for all ports

show paket <PORTLIST> – only for ports in the list

7. Display PoE statistics for all ports

show poe — for all ports

show poe <PORTLIST> – only for ports in the list

#### 5.4.4.2 Viewing switch settings

1. Display information about IGMP Snooping (state, ports)

show igmp_snooping

2. Display information about STP

show stp

3. Display information about SNMP

show snmp

For SNMP v1:

For SNMP v3:

4. Display information about Syslog protocol

show syslog

5. Display VLAN settings

show vlan all – display the list of all VIDs

show vlan 1 – display information for a specific VID

6. Display information about SNTP settings

show sntp

7. Display information about SMTP settings

show smtp

8. Display information about protection from hanging

show autorestart

9. Display information about cameras comfort start function

show comfortstart

10. Display information about dry contacts configuration

show dry_cont

11. Display information about TFTP settings

show tftp

12. Display information about event list setting

show events

13. Dsiplay information about QoS

13.1. State

show 802.1p state

13.2. Information about default priorities

show 802.1p default_priority

13.3 Information about CoS priorities

show 802.1p user_priority

13.4. Scheduling modes

show scheduling_mechanism

13.5 Information about ToS (DSCP) priorities

show dscp_mapping

13.6 Information about speed limitation

show bandwidth_control

14. Display full switch configuration (information is displayed 	in the same form as the configuration file described in 	section 5.3.27.3)

show config

15. Information about filtering by MAC address

15.1 Ports state

show mac_filtering port_state

15.2 List of allowed MAC addresses

show mac_filtering allowed

15.3 List of blocked MAC addresses

show mac_filtering blocked

16. Information about inputs state on the extension board

show inputs

17. Information about outputs state on the extension board

show outputs

18. Information about RS485 settings on the extension board

show rs485 settings

### 5.4.5 Firmware update using TFTP

TFortis PSW support firmware update via Telnet using the external TFTP server.

Command for firmware update:

download firmware_fromTFTP <IP> <PATH>

where <IP> is the IP address of the TFTP server

<PATH> is the path to the firmware file

Let's consider the update process in detail.

1. First make sure, that the TFTP server has been started. If not, start it. A common application for Windows OS is Tftpd32. That is why we will consider the update process based on Tftpd32.

The distribution file is available on the website:

http://tftpd32.jounin.net/tftpd32.html

Start in TFTP server mode

As you can see, the TFTP server will be accessible at the address 192.168.0.104, and the root directory of the server is D:\Pub

2. We put the firmware file in the root directory of the server

3. On the server side, everything is ready. Let's proceed to the switch settings.

By default, the TFTP protocol on the PSW switches is disabled,

enable it using the command:

config tftp state enable

The protocol support will be enabled. In order to save this setting in the non-volatile memory, we execute the save command, otherwise after the reboot this setting will not be saved.

Check that the switch "sees" the TFTP server.  To do this, you can ping

192.168.0.104

4. Proceed to update.

Enter the command:

download firmware_fromTFTP 192.168.0.104 1/PSWupdate407-013-25122014.img

The file will start uploading the file to the internal memory of the switch, after that the update process will start

Then the switch will update the software and reboot, the Telnet connection will be interrupted.

The update process lasts about 1 minute. After that, you can reconnect via Telnet and check the firmware version, making sure that the update was successful.

### 5.4.6 Saving and loading configuration and log via TFTP

PSW switches support saving current switch settings to a configuration file, this file editing and restoring settings from the file.

#### 5.4.6.1 Saving configuration

Configuration is saved to the specified TFTP server

upload cfg_toTFTP <IP> <PATH>

where <IP> is the IP address of the TFTP server

<PATH> is the name and path of configuration

#### 5.4.6.2 Restoring configuration

Configuration is restored from the specified server

download cfg_fromTFTP <IP> <PATH>

where <IP> is the IP address of the TFTP server

<PATH> is the path to the configuration file

After configuration is installed, the switch will restart with the new settings.

#### 5.4.6.3 Saving system log

In some cases, it may be necessary to save the log of the device for later analysis.

upload log_toTFTP <IP> <PATH>

where <IP> is the IP address of the TFTP server

<PATH> is the path to the configuration file

### 5.4.7 Saving settings

Saving settings to a non-volatile memory.

Save

### 5.4.8 Reboot

Rebooting the switch

reboot

### 5.4.9 Exit the management mode

Exit Telnet management mode

exit

### 5.4.10 Diagnostic functions

#### 5.4.10.1 Ping utility

It allows to ping the remote node

ping <IP>

where <IP> is the node IP address

If the node is available:

If the node is not available:

#### 5.4.10.2 Cable tester

cable_diag ports <PORT_LIST>

<PORT_LIST> – the port on which the diagnostics are performed

The cable tester is used to monitor the integrity of the UTP/FTP cable on Fast Ethernet ports.

PSW switches support the function of checking the integrity of the cable on the Fast Ethernet ports. This test determines the type of fault (cutoff or short circuit) for each pair, and also specify the distance from the switch to the fault location.

The physical principle of testing relies on the fact that the switch sends a test electrical impulse over the cable, and on the basis of the delay time and the phase of the received reflected signal determines the distance to the fault and its type.  	For that period of time, the connection and the link on the tested port are intermitted.

If the cable is fault-free and the properly functioning network device is connected to the other side, it is not possible to measure cable length this way, because test signal will be terminated by the end device and will not be a reflection.

Possible testing results:

Short – Short circuit between pairs

Open – Break or cable is not connected

Good – there is no fault.

Examples of cable tester operation

Result in case of cable break:

Result in case of short circuit:

Result in case of normal cable termination:

## 5.5 Management via USB console

TFortis SWU switches have a USB Type-B port on the right of the front panel. This port may be used to connect a console.

To do that, first install the necessary drivers available at http://tfortis.ru/en

Then, when connected to a computer, the system will detect a new device – a virtual COM port.

Figure 5.5.1 Detected device

Now you can connect to COM18 by any terminal, for example PuTTY, selecting the following settings:

speed: 		115200

data bit:		8

stop bits:		1

parity:		no

Figure 5.5.2 Connection settings

After connecting, you will see a "black window". The terminal is in the so-called "diagnostic" mode.

Figure 5.5.3 Terminal window

To switch to console mode, you need to press the Latin "c" key on the keyboard. After that, the console will switch from the diagnostic mode to the command line mode.

Figure 5.5.4 Terminal window in CLI mode

# 6 Technical support

To get technical support for the design of video surveillance systems, operation and adjustment of equipment:

- call (8 a.m. to 4 p.m. Moscow time)

+7 342 260 20 30

- e-mail at:

tfortis@fort-telecom.ru

- use Help-Desk:

http://support.fort-telecom.ru/

All technical documents are available at:

http://www.tfortis.ru/support/documentaciya/

If you have any ideas for improvement or creating new devices, you can send us a request at:

tfortis@fort-telecom.ru

# Comments

In Russian