Operation manual for
PSW-2G8F+

Multifunctional Gigabit Managed Switch
with PoE+ (IEEE802.3at)
for IP- video surveillance systems

Version 4

Warning!

Components of power supply units are under high voltage. Touching conducting components of active power supply units is strictly forbidden.

Warning!

Do not connect the computer to the port that has the “TH” jumper installed.

Warning!

If you do not use TFortis TH camera housings, remove jumpers “TH”.

Warning!

Max load over PoE must be less than 160W.

Warning!

SFP port operates only at 1000 Mbit/s. Fast Ethernet SFP modules will not operate.

For effective operation of lightning protection is required:

- high quality grounding according to the ELC;

- use of shielded twisted pair with shielded connectors RJ45;

- minimization of twisted pair and power cable length;

Table of Contents

1.	Designation	5

2. Features…………………………………………………………………………6

3. 	Description	8

3.1. 	Appearance	6

3.2	Element arrangement	8

3.3	Power Supply over PoE	9

3.4.	Optical Distribution Frame	11

3.5	Tamper sensor	11

3.6	Dry contact	12

3.7 	Lightning protection	13

3.8	Additional functions	14

3.8.1.	Cold start…………………………………………………………………14

3.8.2.	Restart of video cameras at their hanging……………………………14

3.9	Diagnostic functions	15

3.9.1.	Cable tester	15

3.9.2.	Remote polling of video cameras……………………………………..15

4	Technical parameters	17

5	Operation conditions	17

6	Presetting	18

6.1.	Restore switch to Factory Settings	18

6.2.	Setting the IP address	18

6.3.	Setting Up Username and Password	19

6.4.	Configuring PoE on ports	19

6.5.	Enabling Preheating of camera housings	21

6.6.	Enabling backup protocols	21

7. 	Device installation…………………………………………………..	……22

7.1.	Unit mounting…………………………………………..…………………22

7.2.	Mounting on the support…………………………………………………23

7.3.	Mounting in a cabinet…………………………………………………….23

7.4	Optic connection	24

7.5	Power connection	24

7.5.1.   Main power supply……………………………………………………..24

7.5.2.   	Backup power supply………………………………………………….25

7.6	Connection of video cameras	25

- Manufacturer’s warranty	26

9.  Technical support……………………………………………………………26

- Designation

PSW-2G8F+ device is an Outdoor Multifunctional Gigabit Managed Switch with built-in optical distribution frame. Designed for networking of IP- video surveillance systems.

Figure 1. Connection diagram for the PSW-2G8F+

- Features

Weatherproof version

The body of the device is made of a techno-polymer that is resistant to Stringent Operating Conditions. There is a protection from moisture and dust IP66.

Operation in extreme temperatures

The device has industrial hardware components that are characterized by an extended temperature range. Using industrial SFP modules in industrial version guarantees operation from -60°C to 50°C* and above, up to +70°C with less load.

*The maximum temperature depends on the load (see diagram in section 5. Operation conditions)

High- performance gigabit switch

The basis of the switch is a high-performance chip from Marvell, which provides processing of a large traffic coming from IР-video cameras.

PoE+ Support

All ports of the switch support PoE+ (IEEE802.3at), which made it possible to transmit up to 30W to video camera via ordinary twisted pair.

Power supply for Camera housings over PoE

Switch operating with TFortis TH camera housings powers both video camera and Camera Housing via PoE.

Built-in Optical Distribution Frame

Presence of the Optical Distribution Frame allows distributing optics inside the device and connecting it to SFP modules.

Tamper sensor

There is an optical Tamper sensor inside the device for the detection and timely notification of unauthorized access.

Connection to 230VAC

Built-in power supply unit provides direct connection to the Power Supply 230VAC and excludes need in additional PSU. The unit provides place for installation of the Circuit Breaker.

Lightning protection

Built-in Lightning protection of Ethernet ports and 230V PSU reliably protects both the switch and connected video cameras from pulse disturbances induced by lightning discharges.

Cold start

Preheating of camera housings provides safe and guaranteed turn-on of video cameras in cold conditions.

Automatic restart of video cameras at their hanging

The switch controls operation of video cameras. If video camera is hanging, switch restart it automatically over PoE. This allows constructing unattended IP- video surveillance systems.

Management via WEB-interface

A user-friendly and intuitive interface allows you quickly and easily configure the system.

Operation in a ring and in a chain

With two gigabit ports, you can connect the switches in a line topology. STP/RSTP protocol support allows creating ring topologies, what significantly increases the fault tolerance of the system.

Figure 2.1-1. PSW-2G8F+ outside view

Figure 2.1-2. PSW-2G8F+ inside appearance

Figure 2.1-3. PSW-2G8F+ disassembled

  - Element arrangement

Figure 3.2. Element arrangement of PSW-2G8F+

During normal operation of the processor, a CPU indicator must light intermittently with a frequency of 2s. (1 sec. - on, 1 sec. - off.) DEFAULT Indicator is on, when the device is in factory settings (IP 192.168.0.1).

  - Power Supply over PoE

№1 and №2 ports

№1 and №2 ports of PSW-2G8F+ supports double PoE+ (IEEE 802.3at) up to 60W. 30W is transmitted over wire pairs 1,2 and 3,6 (mode A) and also 30W is transmitted over pairs 4,5 and 7,8 (mode B) simultaneously. As a result, the total load is 60W. This power scheme is supported by energy-intensive devices. For example, outdoor PTZ-cameras with a declared capacity of 60W. (see I, figure 3.3)

IMPORTANT! If you connect TFortis TH camera housings to 1 and 2 ports, make the configuration via WEB interface (PoE_A=auto, PoE_B=Passive).

№3 .. №6 ports

Ports from №3 to №6 of PSW-2G8F+ supports PoE+ (IEEE 802.3at) up to 30W. The choice of the power option is determined by the configuration of jumpers (Table 3-3).

Table 3-3. PoE jumpers configuration

|  | 1,2 and 3,6 Pairs | 4,5 and 7,8 Pairs | Position |
| --- | --- | --- | --- |
|  | IEEE802.3at (video camera) | Passive PoE (TFortis TH camera housing) | IV |
|  | IEEE802.3at (video camera) | - | III |
|  | - | IEEE802.3at (video camera) | II |
|  | - | - |  |

IMPORTANT! If you do not use TFortis TH camera housings, be sure to remove jumpers “TH”. If you don’t do this, the video camera will “pick up” the power that is intended for the camera housing. In this case, the camera will not be automatically restarted when it hangs.

If you use the TFortis TH camera housings, check that jumpers are in position “A” and “TH” for the corresponding port. In this case, the video camera will receive power over pairs 1,2 and 3,6, and camera housings over pairs 4,5 and 7,8.

Since the PoE+ standard is backward compatible with simple PoE, the switch will power any IEEE802.3af video camera with up to 15W consumption.

  - Optical Distribution Frame

Figure 3.4. Optical Distribution Frame

Warning! Accessories for fiber optic welding (shrinkable plastic sleeves, pigtails, ties, etc.) are not supplied.

  - Tamper sensor

There is an Optical Tamper sensor inside the device (Figure 3.5-1). Unlike magnetically operated sealed switches and end switches, optical switch is more reliable. It does not stick, does not give a rattling. An operating principle is simple. When the unit is closed, special detector (Figure 3.5-2) installed on the unit cover breaks the optical flow. When the unit is opened, the detector exits from the sensor and activates it.

Figure 3.5-1. Tamper sensor on the board

Figure 3.5-2. The door of the tamper sensor on the unit cover

IMPORTANT! Make sure that you correctly orient the cover of the unit when you close it. The detector should fall between tamper sensor beads.

  - Dry contact

Dry contacts are intended for connection of external sensors (magnetically operated sealed switch, end switch, motion sensor with relay-controlled output, etc.). Pin 1 has a universal screw terminal. Pin 2 is for connecting the HU-2 terminal (the terminal for the cable is optional). The state of “normally closed” or “normally open” is set via the WEB interface.

Figure 3.6 Dry contacts

3.7 Lightning protection

The PSW-2G8F+ switch has in-built lightning protection modules that provide protection of Ethernet ports and power supply circuits 230VAC from common-mode and differential electromagnetic disturbances.

Switches are resistant to high-energy microsecond pulse interference in accordance with GOST R 51317.4.5 standard with a degree of rigidity according to Table 3.7-1 with performance criteria B.

Switches are resistant to dynamic changes in the voltage of the AC electrical network in accordance with GOST R 51317.4.11 standard according to Table 3.7-2 with the performance criteria B.

Table 3.7-1.

| Port | Degree of rigidity according to the table 1 of standard GOST R 51317.4.5 | Voltage pulse value, kW + 10% |
| --- | --- | --- |
| Power lines of the switch “wire-wire” | 3 | 2 |
| Power lines of the switch “wire-ground” | 4 | 4 |
| Symmetrical communication lines of the switch “wire-ground” | 3 | 2 |

Table 3.7-2.

| Types of impacts | Degree of rigidity at testing | Test voltage, % Ur, + 5 % | Amplitude of dynamic voltage changes, % Ur | Duration of dynamic voltage changes, periods (ms) |
| --- | --- | --- | --- | --- |
| Voltage dips | 1 | 70 | 30 | 10 (200) |
| Voltage interruptions | 1 | 0 to 20 | 100 | 1 (20) |
| Voltage surge | 2 | 120 | 20 | 25 (500) |
| Note - Ur - rated supply voltage. |

  - Additional functions

    - Cold start

The most critical moment in the operation of the video camera is the process of its activation at low ambient temperature. Precisely a cold start can cause the failure of an expensive video camera. To avoid such cases, unit PSW-2G8F+ is implemented with preheating of TFortis TH camera housings. The essence of it is that after power is applied to the unit, initially will be powered heating elements of camera housings, and only then in 1 hour, the video camera itself. This delay allows obtaining comfortable conditions for starting video cameras and you will be able to save expensive equipment. Option Comfort Start is available via WEB-interface in the section Special Function.

(Performance criterion B - temporary deterioration in the performance quality or termination of the established function with the subsequent restoration of normal functioning, carried out without the operator’s intervention) Maintainability is preserved during fluctuations in supply voltage from ~ 187 to ~ 253 V

    - Restart of video cameras at their hanging

The PSW-2G8F+ constantly monitors the connection of the video camera to the switch. There are three ways to determine the camera’s hanging:

- No connection to the video camera (Link)

- No response to service requests (Ping)

- Reducing the flow from the camera (Speed)

Video camera restart over the Link signal.

The PSW-2G8F+ switch constantly (1 time per minute) monitors the Link signal from the IP camera. If the switch does not detect the Link signal, then it starts a one-minute timer, when it ends, the connection is reconnected. If the Link signal does not appear, the PSW-2G8F+ removes power for 10 seconds and resets it, rebooting the camera. This mechanism can be described in other words. If the switch has not seen the Link signal from the video camera twice in a row with a 1-minute interval, then it reboots it. Option Auto Restart is available via WEB-interface in the section Special Function.

Video camera restart when there is no response to Ping.

The PSW-2G8F+ switch constantly (1 time per minute) polls the IP camera. If the switch does not receive a response, then starts a one-minute timer, during which the poll is repeated every 10 seconds. If the video camera does not response within a minute, the PSW-2G8F+ removes power for 10 seconds and resets it, rebooting the camera. If the camera has responded at least once, the switch decides that the camera is functioning properly and will start the poll cycle once again, referring to the camera 1 time per minute. Option Auto Restart is available via WEB-interface in the section Special Function. To use this mechanism, you will need to enter the IP address of your video camera. Make sure your video camera is responding to the PING (see diagnostic functions section).

Video camera restart when reducing the flow from the camera

The PSW-2G8F+ switch constantly controls traffic level (intensity) from the camera. If the activity falls below the set level the switch restarts the camera by removing power from the PoE. This function is enabled via WEB interface for a specific port.

  - Diagnostic functions

    - Cable tester

The PSW-2G8F+ has functions of a virtual cable tester (VCT - Virtual Cable Tester), which allows you to determine the break of the twisted pair, short-circuited twisted pair wires, unconnected cable to the video camera, distance between the defect and the switch. A cable tester diagnoses pairs that transmit data (1, 2 и 3, 6). Please note that the accuracy of the cable tester is ±2 meters.

By default, VCT operates on an average algorithm and does not take into account the specific features of a particular cable, which can affect the accuracy of the measurement. To improve the accuracy of the cable tester, it is recommended to calibrate it. Note that calibration is not recommended for cables with a length of less than 10 meters.

    - Remote polling of video cameras

With the PSW-2G8F+ it is possible to ping any device in the network via the WEB-interface, which is convenient when solving network problems.

  - Power supply backup

There are two power supply inputs in PSW-2G8F+ switch. The main power supply (230 VAC) is put on the power supply unit, the backup power supply (54 VDC) is directly connected to the switch board. When the main power is lost, the device continues to work due to backup power. It is possible to use the device without power supply backup.

- Technical parameters

Gigabit Ethernet Ports

- 1000Base-X with SFP connector;

- Number of ports - 2 pcs.;

Fast Ethernet Ports

- 10/100Base-Tx with RJ-45 connector;

- number of ports - 8;

- supports Auto-MDIX for the 10/100Base-Tx port;

- supports flow control of IEEE 802.3x;

- supports IEEE802.3at according to mode “A” or “B” up to 30W;

- supports Passive PoE by mode B - 30W;

- maximum output power for all ports (PoE budget) - 160W;

- transmission distance – up to 100m.

Main power supply

- unit supply voltage – 230VAC (from 187V to 253V);

- max power consumption 200W;

Backup power supply

- unit supply voltage – 54V DC (from 53V to 55V);

- max power consumption 170W;

Design

- Dimensions 240x360x120 mm;

- Maximum weight 4 kg;

- protection level against the external influences IP66;

- number of cable glands for cable diameter 4-8 mm – 9 pcs, 6-12 mm – 2 pcs.

Reliability

- mean time between failures is more than 75 000 hours (8,6 years).

- Operation conditions

The switch PSW-2G8F+ is intended for 24-hour outside operation at ambient temperature from -60 to +50°C* and above using industrial SFP modules, up to +70°C with less load.

*The maximum temperature depends on the load (see diagram)

The switch PSW-2G8F+ maintains declared parameters at storage temperatures from -60C to +50C (-67 F to 122 F).

It is recommended to install the switch in places protected from direct sunlight (for example, under canopies, on the shady side of buildings)

- Presetting

  - Restore switch to Factory Settings

Before starting work, put the PSW-2G8F+ switch into the default settings. For this, you should press and hold DEFAULT button until DEFAULT indicator lights up. Commutator by default has IP-address 192.168.0.1.

  - Setting the IP address

All software functions of the PSW-2G8F+ are available for management, configuration and monitoring using the built-in Web interface. The switch can be managed from remote stations anywhere in the network via a standard Web browser (for example, Microsoft Internet Explorer). The browser is a universal access tool and can directly access the PSW-2G8F+ using the HTTP protocol.

Connect any port on the PSW-2G8F+ to an Ethernet network. Keep in mind that if the device is configured over a network, then the IP address of the management workstation must belong to the same IP network. For example, if, by default, the switch’s IP address is 192.168.0.1, then the IP address of the workstation should be 192.168.0.x (where x is a number from 2 to 254), the default subnet mask is 255.255.255.0.

Open the Web browser and enter the IP address http://192.168.0.1.

Figure 6.2. Entering the IP Address of the switch

  - Setting Up Username and Password

Until the “Username” and “Password” are set, you will log in without entering this data. After the password is set, you will need to pass authentication at logging in.

Figure 6.3. Entering Username and Password.

Note that the Username and the Password are case sensitive.

  - Configuring PoE on ports

PoE configuration is carried out with jumpers (see 3.3 section). All connections must be made with the 230VAC power supply disconnected.

When connecting devices that do not support PoE (for example, a computer), be sure to remove the jumpers from the corresponding port.

  - Enabling Preheating of camera housings

When the camera is turned on in cold conditions, it may not start or, even worse, fail. To solve this problem, use the Comfort Start function: go to the Special Function tab in the Comfort Start section and enable the option. By default it is disabled. This function is available only with TFortis TH camera housings.

IMPORTANT! When this option is enabled, after the power is applied to the switch, the cameras will only turn on after time of Soft Start Time. To force the cameras to turn on, click on Manual Start.

  - Enabling backup protocols

If you connect switches into a ring you need to enable the RSTP protocol. Otherwise, if alternative paths appear, your network will not work. By default, RSTP is disabled.

7. Device installation

  - Unit mounting

The enclosure has four attachment points along the edges of the unit. The marking of the fastening for the installation of the product is shown on the Fig. 7.1.

IMPORTANT! Drilling of the housing leads to the sealing violation of the entire switch and, as a consequence, the loss of warranty.

  - Mounting on the support

PSW-2G8F+ allows outdoor operation in the open air because device enclosure provides IP66 protection rating. When it’s required to install the switch on a support, the switch is mounted on a Bracket for PSW using  a 30 mm bandage tape (https://tfortis.com/products/support-brackets/tfortis-support-bracket-for-psw/). For mounting on a Bracket M4 screws are used.

  - Mounting in a cabinet

When it is required to provide additional vandalism protection, we recommend to install the switch in metal outdoor cabinets TFortis CrossBox-2 and CrossBox-3.

PSW-2G8F+ provides for fixing to the rear false wall of the outdoor cabinet with four M4 screws.

  - Optic connection

Inside the PSW-2G8F+ is installed Optical Distribution Frame. Optical cable is put into large cable glands that are on the lower level of the unit. The optical cable is attached to the metal base of the distribution frame using nylon ties or metal clamps. For attaching the string are used metal columns with screws. Optical fibers fit in a splice-cassette designed for 32 shrinkable plastic sleeves. Welded pigtails are connected to SC adapters located on the plate. The optical patch cords then connect adapters and SFP modules. It is allowed to connect pigtails directly to SFP excluding unnecessary connections.

IMPORTANT! The kit does NOT include nylon ties, shrinkable plastic sleeves, pigtails, adapters.

IMPORTANT! Port SFP operates only at 1000 Mbit/s. SFP modules Fast Ethernet will not operate.

  - Power connection

7.5.1. Main power supply

PSW-2G8F+ is connected to the AC source of 230VAC. The supply cable is brought into the unit through the cable gland and connected to the terminal block of the power supply unit. It is possible to make this connection through a circuit breaker to remove high voltage when maintaining the switch. Calculation of the cable cross-section is based on the maximum consumption of the PSU that does not exceed 200W. Grounding of the device is required. The ground resistance must be no more than 4 Ohm.

IMPORTANT! Do not allow circuit boards contacting high voltage live wires. Failure in this case entails a loss of the warranty.

IMPORTANT! Since the switch contains switch-mode power supplies, it is a reactive load. During start-up, when charging input capacitors, a starting current appears and it exceeds the nominal value. In order to avoid false alarms of the protection devices, it is recommended to choose models with the characteristic C for a current of at least 4A.

6.3.2. Backup power supply

The PSW-2G8F+ has 54V DC backup power. The supply cable is brought into the unit through the cable gland and connected to the terminal block on the switch circuit board. Calculation of the cable cross-section is based on the maximum consumption that does not exceed 170W.

IMPORTANT! The switch can be operated without a backup power supply.

  - Connection of video cameras

To the ports FE, connect cameras using a twisted pair. It is recommended to use a 4-pair shielded cable no worse than Category 5. The PSW-2G8F+ allows you to connect any PoE video camera with one cable, which drastically reduces the complexity of system installation.

The Ethernet cable is inserted through the cable gland into the unit, clipped and connected to the FE ports. For the convenience of clipping, it is allowed to remove the cable gland from the unit and then re-install it back to its original state. Unused cable glands should be closed off.

RJ-45	RJ-45

Figure 6.4. Fanning out of the Ethernet cable.

- Manufacturer’s warranty

Warranty period for the device – 36 months from the sale date. The device is accepted for warranty maintenance and repair only in full completeness.

Warranty repair is not performed in following cases:

- if warranty period has expired;

- if there is no label with serial number on the product housing, and also if serial number was changed, removed or illegible;

- if there are external and internal mechanical damages (chips, cracks, deformation, damage to the power cord, breaks and cracks of connectors), traces of chemicals, corrosive environments, liquids, heavy contamination, as well as the presence of insects or traces of their presence;

- due to non-compliance with the rules of connection and operation, as well as non-compliance of power specified in the operating manual;

- due to force majeure, third party action and other reasons that doesn’t depend on manufacturer.

9. Technical support

Technical support for the design of video surveillance systems, issues of operation and configuration of equipment is provided by email tfortis@fort-telecom.ru

Technical documents are available on the website https://tfortis.com/support/dokumentaciya-na-produkciyu/

# Text boxes

3. Description

3.1. Appearance

Figure 3.3. Scheme of the power supply over PoE for different cases

Figure 7.1. Marking of the fastening

White Orange

Orange

White Green

Blue

White Blue

Brown

White Brown

Green

Brown

White Brown

Green

White Blue

Blue

White Green

Orange

White orange